## Slide 1
Self-Heating in a Cylindrical GAAFET:
from the MOSFET to a Cooler Device
How every device parameter changes on the way from a planar MOSFET to a cooler gate-all-around transistor
cylindrical GAAFET cross-section
Nithyanand B
CB.EN.P2VLD26021
Priyadharshini K
CB.EN.P2VLD26025
Sivaprakash R
CB.EN.P2VLD26027
M.Tech VLSI Design · Analog VLSI and Device Modelling Lab (25VL681)
Notes: Our project studies heat in gate-all-around transistors. We start from the ordinary MOSFET and follow every key parameter as the device changes: planar, FinFET, GAA. Then we show the heat problem GAA brings, reproduce one base paper in Silvaco Atlas, and propose a cooler device.

## Slide 2
Abstract
In one line: we follow a transistor from planar to gate-all-around, then make it run 16 % cooler
Problem
Short planar MOSFETs leak: the drain, not the gate, starts to control the channel.
Industry fix
Wrap the gate around the channel: planar → FinFET → gate-all-around (GAA).
New problem
The oxide wrapped around the channel conducts heat 10–100× worse than silicon.
Base paper
Chen et al., IEEE EDTM 2025: a 3-nm GAA NMOS heats by 64.8 K at 30 µW.
What we did
Built a cylindrical GAAFET in Silvaco Atlas 3D, matched the paper, tried four cooler designs.
Result
68.0 K vs 64.8 K (+5 %). Design D: 16.4 % cooler, 2.5× less leakage, −7.8 % on-current.
The journey in six steps
1
MOSFET
leaks
DIBL 202 mV/V
2
FinFET
3 sides
DIBL 62 mV/V
3
GAAFET
all round
DIBL 41 mV/V
4
Heat
trapped
ΔT 64.8 K
5
Reproduce
+5 %
68.0 K
6
Optimal
cooler
−16.4 % ΔT
Better gate control brought a heat problem; we measure it, match the paper, then lower it.
Notes: Short MOSFETs leak. GAA fixes this by wrapping the gate around the channel, but the oxide that wraps it also traps heat. We pick one base paper, build a GAAFET, reproduce its self-heating within 5 percent, then design a device that runs 16.4 percent cooler.

## Slide 3
Contents
01
The MOSFET switch
Build it · turn the gate · turn the drain · VT and SS in depth
02
Shrinking the gate
Shorter Lg · DIBL and leakage · the scale length λ
03
FinFET → GAAFET
More gate sides · fin width · wire, sheet, stack · our GAA in numbers
04
The new problem: heat
Oxide traps heat · ΔT = Rth · P · what heat does to every metric
05
Literature and method
Five papers · base paper Chen et al. 2025 · Silvaco Atlas flow
06
Three stages in TCAD
Standard GAAFET · reproduce the paper · optimal design D
07
Conclusion
Gains and limits · the whole story · next steps
Notes: Seven chapters. Each later chapter changes one thing about the transistor and shows how the key numbers move.

## Slide 4
Contents
01
The MOSFET switch
Build it · turn the gate · turn the drain · VT and SS in depth
02
Shrinking the gate
Shorter Lg · DIBL and leakage · the scale length λ
03
FinFET → GAAFET
More gate sides · fin width · wire, sheet, stack · our GAA in numbers
04
The new problem: heat
Oxide traps heat · ΔT = Rth · P · what heat does to every metric
05
Literature and method
Five papers · base paper Chen et al. 2025 · Silvaco Atlas flow
06
Three stages in TCAD
Standard GAAFET · reproduce the paper · optimal design D
07
Conclusion
Gains and limits · the whole story · next steps
Chapter 01
The MOSFET switch
Build it
turn the gate
turn the drain
VT and SS in depth
Notes: Chapter 1: how the planar MOSFET works and which numbers describe it.

## Slide 5
The MOSFET – How it is built
Side view of a planar n-channel MOSFET, built one layer at a time
p-type silicon (body)
1
Start with p-type silicon
A crystal of silicon doped with boron: holes are the majority carriers. No current can flow from left to right yet.
Every transistor starts as a block of lightly doped silicon.
Notes: A crystal of silicon doped with boron: holes are the majority carriers. No current can flow from left to right yet.

## Slide 6
The MOSFET – How it is built
Side view of a planar n-channel MOSFET, built one layer at a time
p-type silicon (body)
n+ source
n+ drain
2
Add n+ source and drain
Two heavily doped n-type islands full of free electrons. Between them: p-type silicon, which blocks electrons.
Source and drain are full of electrons; the p-type gap between them blocks them.
Notes: Two heavily doped n-type islands full of free electrons. Between them: p-type silicon, which blocks electrons.

## Slide 7
The MOSFET – How it is built
Side view of a planar n-channel MOSFET, built one layer at a time
p-type silicon (body)
n+ source
n+ drain
gate
3
Add oxide and gate
A thin insulator and a metal gate sit over the gap. The gate cannot touch the channel, it can only push on it with an electric field.
The gate controls the gap through the oxide, like one plate of a capacitor.
Notes: A thin insulator and a metal gate sit over the gap. The gate cannot touch the channel, it can only push on it with an electric field.

## Slide 8
The MOSFET – How it is built
Side view of a planar n-channel MOSFET, built one layer at a time
p-type silicon (body)
n+ source
n+ drain
gate
VS = 0
VG = 0.00 V
VD = 0.70 V
electron energy ↑
4
The energy hill
Seen as energy, the p-type gap is a hill between source and drain. Electrons cross only if the hill is low. The gate sets the hill height.
A MOSFET is an energy hill whose height is set by the gate.
Notes: Seen as energy, the p-type gap is a hill between source and drain. Electrons cross only if the hill is low. The gate sets the hill height.

## Slide 9
The MOSFET – Turning the gate
One knob, VG: the device, the energy hill and the current change together
p-type silicon (body)
n+ source
n+ drain
gate
VS = 0
VG = 0.00 V
VD = 0.70 V
electron channel
depletion (no free carriers)
electron energy ↑
0
0.2
0.4
0.6
100 pA
10 nA
1 µA
100 µA
gate voltage VG (V)
ID (log: each line = 100×)
VT
166 pA
VG = 0.00 V ID = 166 pA
OFF: only leakage Ioff
KNOB: gate voltage VG 0.0 V
0.0
0.2
0.4
0.6
0.7
VG = 0: the hill is high and there is no channel. Only a tiny leakage flows.
Notes: Left: the transistor and its energy hill. Right: the I_D–V_G curve on a log scale. All three move together as the gate voltage is raised. Model curve: EKV, V_T = 0.25 V, SS = 71 mV/dec, V_D = 0.7 V.

## Slide 10
The MOSFET – Turning the gate
One knob, VG: the device, the energy hill and the current change together
p-type silicon (body)
n+ source
n+ drain
gate
VS = 0
VG = 0.20 V
VD = 0.70 V
electron channel
depletion (no free carriers)
electron energy ↑
0
0.2
0.4
0.6
100 pA
10 nA
1 µA
100 µA
gate voltage VG (V)
ID (log: each line = 100×)
VT
76 nA
VG = 0.20 V ID = 76 nA
SUBTHRESHOLD: current grows ×10 every 71 mV
KNOB: gate voltage VG 0.2 V
0.0
0.2
0.4
0.6
0.7
Gate up: the hill drops and current rises exponentially, still below VT.
Notes: Left: the transistor and its energy hill. Right: the I_D–V_G curve on a log scale. All three move together as the gate voltage is raised. Model curve: EKV, V_T = 0.25 V, SS = 71 mV/dec, V_D = 0.7 V.

## Slide 11
The MOSFET – Turning the gate
One knob, VG: the device, the energy hill and the current change together
p-type silicon (body)
n+ source
n+ drain
gate
VS = 0
VG = 0.30 V
VD = 0.70 V
electron channel
depletion (no free carriers)
electron energy ↑
0
0.2
0.4
0.6
100 pA
10 nA
1 µA
100 µA
gate voltage VG (V)
ID (log: each line = 100×)
VT
778 nA
VG = 0.30 V ID = 778 nA
THRESHOLD CROSSED: the channel forms
KNOB: gate voltage VG 0.3 V
0.0
0.2
0.4
0.6
0.7
Past VT = 0.25 V a thin electron layer joins source and drain: the switch turns on.
Notes: Left: the transistor and its energy hill. Right: the I_D–V_G curve on a log scale. All three move together as the gate voltage is raised. Model curve: EKV, V_T = 0.25 V, SS = 71 mV/dec, V_D = 0.7 V.

## Slide 12
The MOSFET – Turning the gate
One knob, VG: the device, the energy hill and the current change together
p-type silicon (body)
n+ source
n+ drain
gate
VS = 0
VG = 0.40 V
VD = 0.70 V
electron channel
depletion (no free carriers)
electron energy ↑
0
0.2
0.4
0.6
100 pA
10 nA
1 µA
100 µA
gate voltage VG (V)
ID (log: each line = 100×)
VT
3.5 µA
VG = 0.40 V ID = 3.5 µA
STRONG INVERSION: channel thickens
KNOB: gate voltage VG 0.4 V
0.0
0.2
0.4
0.6
0.7
More gate, thicker channel; the curve bends because the channel now acts like a resistor.
Notes: Left: the transistor and its energy hill. Right: the I_D–V_G curve on a log scale. All three move together as the gate voltage is raised. Model curve: EKV, V_T = 0.25 V, SS = 71 mV/dec, V_D = 0.7 V.

## Slide 13
The MOSFET – Turning the gate
One knob, VG: the device, the energy hill and the current change together
p-type silicon (body)
n+ source
n+ drain
gate
VS = 0
VG = 0.70 V
VD = 0.70 V
electron channel
depletion (no free carriers)
electron energy ↑
0
0.2
0.4
0.6
100 pA
10 nA
1 µA
100 µA
gate voltage VG (V)
ID (log: each line = 100×)
VT
29.8 µA
VG = 0.70 V ID = 29.8 µA
ON: full current Ion
KNOB: gate voltage VG 0.7 V
0.0
0.2
0.4
0.6
0.7
VG = VDD = 0.7 V: thick channel, low hill, the full on-current Ion.
Notes: Left: the transistor and its energy hill. Right: the I_D–V_G curve on a log scale. All three move together as the gate voltage is raised. Model curve: EKV, V_T = 0.25 V, SS = 71 mV/dec, V_D = 0.7 V.

## Slide 14
The MOSFET – Reading the switch
From the ID–VG curve we read the numbers that the rest of the project tracks
0
0.1
0.2
0.3
0.4
0.5
0.6
0.7
100 pA
10 nA
1 µA
100 µA
gate voltage VG (V)
ID (log)
VD = 0.7 V
Ioff
Ion
Metric
What it tells
Good is
Ion
current when on: speed
large
Ioff
leakage when off: standby power
small
VT
gate voltage where it turns on
set by design
SS
mV of VG for 10× current
→ 60 mV/dec
DIBL
how much the drain moves VT
small
Two currents first: Ion (speed) and Ioff (leakage). Their ratio is the switch quality.
Notes: Every later result in the project is one of these five numbers, plus the temperature rise.

## Slide 15
The MOSFET – Reading the switch
From the ID–VG curve we read the numbers that the rest of the project tracks
0
0.1
0.2
0.3
0.4
0.5
0.6
0.7
100 pA
10 nA
1 µA
100 µA
gate voltage VG (V)
ID (log)
VD = 0.7 V
Ioff
Ion
VT
SS: mV per ×10
Metric
What it tells
Good is
Ion
current when on: speed
large
Ioff
leakage when off: standby power
small
VT
gate voltage where it turns on
set by design
SS
mV of VG for 10× current
→ 60 mV/dec
DIBL
how much the drain moves VT
small
Then two voltages: VT says where the switch turns on, SS how sharply.
Notes: Every later result in the project is one of these five numbers, plus the temperature rise.

## Slide 16
The MOSFET – Reading the switch
From the ID–VG curve we read the numbers that the rest of the project tracks
0
0.1
0.2
0.3
0.4
0.5
0.6
0.7
100 pA
10 nA
1 µA
100 µA
gate voltage VG (V)
ID (log)
VD = 0.7 V
VD = 0.05 V
DIBL = shift ÷ ΔVD
Ioff
Ion
VT
SS: mV per ×10
Metric
What it tells
Good is
Ion
current when on: speed
large
Ioff
leakage when off: standby power
small
VT
gate voltage where it turns on
set by design
SS
mV of VG for 10× current
→ 60 mV/dec
DIBL
how much the drain moves VT
small
DIBL compares two drain voltages: it shows if the drain is stealing control from the gate.
Notes: Every later result in the project is one of these five numbers, plus the temperature rise.

## Slide 17
The MOSFET – What sets VT
Energy bands from the gate (left) through the oxide into the p-type silicon (right)
gate metal
oxide
p-type silicon
EC
Ei
EV
EF
EF (metal)
VG = -0.47 V
band bending ψs = 0.00 V
1
Term 1: flat-band voltage VFB
Gate metal and silicon have different work functions: φm = 4.50 eV, φs = 4.97 eV.
VFB = φm − φs = −0.47 V keeps the bands flat.
Higher φm → higher VT, one to one.
VT =
VFB
+
2φF
+
Qdep / Cox
VFB is set by the gate metal: it is the gate voltage that keeps the bands flat.
Notes: Gate metal and silicon have different work functions: φm = 4.50 eV, φs = 4.97 eV. V_FB = φm − φs = −0.47 V keeps the bands flat. Higher φm → higher V_T, one to one.

## Slide 18
The MOSFET – What sets VT
Energy bands from the gate (left) through the oxide into the p-type silicon (right)
gate metal
oxide
p-type silicon
EC
Ei
EV
EF
EF (metal)
VG = 0.00 V
band bending ψs = 0.35 V
2
Raise VG: the bands bend
A positive gate pulls the bands down at the surface.
Holes are pushed away: a depletion layer (pink) of fixed negative ions grows.
VT =
VFB
+
2φF
+
Qdep / Cox
Raising VG bends the bands; the surface loses its holes.
Notes: A positive gate pulls the bands down at the surface. Holes are pushed away: a depletion layer (pink) of fixed negative ions grows.

## Slide 19
The MOSFET – What sets VT
Energy bands from the gate (left) through the oxide into the p-type silicon (right)
gate metal
oxide
p-type silicon
EC
Ei
EV
EF
EF (metal)
VG = 0.25 V
band bending ψs = 0.71 V
3
Term 2: invert the surface, 2φF
φF = (kT/q)·ln(NA/ni) = 0.357 V for NA = 10¹⁶ cm⁻³.
Bend by 2φF = 0.71 V: the surface is as n-type as the body is p-type.
Electrons fill the surface: threshold.
VT =
VFB
+
2φF
+
Qdep / Cox
At 2φF of band bending electrons gather at the surface: that is threshold.
Notes: φF = (kT/q)·ln(N_A/n_i) = 0.357 V for N_A = 10¹⁶ cm⁻³. Bend by 2φF = 0.71 V: the surface is as n-type as the body is p-type. Electrons fill the surface: threshold.

## Slide 20
The MOSFET – What sets VT
Energy bands from the gate (left) through the oxide into the p-type silicon (right)
gate metal
oxide
p-type silicon
EC
Ei
EV
EF
EF (metal)
+
+
+
+
−
−
−
−
VG = 0.25 V
band bending ψs = 0.71 V
4
Term 3: charge on the capacitor
The depletion layer holds negative ions; the gate must hold the same + charge.
Vox = Qdep / Cox: planar 11 mV, our GAA wire only 0.1 mV (tiny body).
VT =
VFB
+
2φF
+
Qdep / Cox
Gate and silicon form a capacitor; holding the depletion charge costs Qdep/Cox.
Notes: The depletion layer holds negative ions; the gate must hold the same + charge. V_ox = Q_dep / C_ox: planar 11 mV, our GAA wire only 0.1 mV (tiny body).

## Slide 21
The MOSFET – What sets VT
Energy bands from the gate (left) through the oxide into the p-type silicon (right)
gate metal
oxide
p-type silicon
EC
Ei
EV
EF
EF (metal)
+
+
+
+
−
−
−
−
VG = 0.25 V
band bending ψs = 0.71 V
5
Add them up
VT = −0.47 + 0.71 + 0.011 = 0.26 V (long-channel estimate).
Atlas, our GAAFET: 0.204–0.209 V.
Short-channel effects (DIBL) pull it a little lower.
VT =
VFB
+
2φF
+
Qdep / Cox
Long-channel estimate 0.26 V vs Atlas 0.20 V: the physics checks out.
Notes: V_T = −0.47 + 0.71 + 0.011 = 0.26 V (long-channel estimate). Atlas, our GAAFET: 0.204–0.209 V. Short-channel effects (DIBL) pull it a little lower.

## Slide 22
The MOSFET – What moves VT
Five knobs in our project, which way each one pushes VT, and by how much
▲
VT
Gate work function φm
+0.03 eV → VT +30 mV
Atlas: 0.204 → 0.233 V. Our stage-3 knob.
▲
VT
Channel doping NA
more doping → higher VT
Our wire is light: 10¹⁶ cm⁻³.
▼
VT
Temperature (self-heating)
≈ −1.6 mV/K (planar estimate)
300 → 343.6 K: VT falls, Ioff rises.
▼
VT
Drain voltage (DIBL)
−38 mV per V of VD
Reproduced wire, from Atlas.
▼
VT
Wire radius r
thicker wire → weaker grip
r 4 → 5.64 nm: DIBL 17 → 38 mV/V.
For our project
Stage 3 raises φm a little (+30 mV VT) to cut Ioff and power P, so less heat. A cooler channel then keeps VT stable.
Work function is our VT knob; heat and DIBL pull VT down and raise leakage.
Notes: These are the knobs that move threshold in this project. Work function and doping raise it; temperature, drain voltage and a thicker wire lower it.

## Slide 23
The MOSFET – Why SS can never beat 60 mV/dec
Two facts give the limit: the barrier rule and a capacitor divider
gate VG
Cox (gate oxide)
ψs (hill height)
Cdep (depleted body)
body / source
1
Barrier rule
ID ∝ exp(qψs / kT): the current depends only on the hill height ψs.
Current depends only on the hill height ψs.
Notes: Proof in four steps. Gate-all-around brings m close to 1, which is why our devices are near 60 mV/dec.

## Slide 24
The MOSFET – Why SS can never beat 60 mV/dec
Two facts give the limit: the barrier rule and a capacitor divider
gate VG
Cox (gate oxide)
ψs (hill height)
Cdep (depleted body)
body / source
1
Barrier rule
ID ∝ exp(qψs / kT): the current depends only on the hill height ψs.
2
10× current needs 59.5 mV
Δψs = (kT/q)·ln10 = 25.85 mV × 2.303 = 59.5 mV at 300 K.
10× current needs the hill to drop by 59.5 mV.
Notes: Proof in four steps. Gate-all-around brings m close to 1, which is why our devices are near 60 mV/dec.

## Slide 25
The MOSFET – Why SS can never beat 60 mV/dec
Two facts give the limit: the barrier rule and a capacitor divider
gate VG
Cox (gate oxide)
ψs (hill height)
Cdep (depleted body)
body / source
Δψs = ΔVG · Cox / (Cox + Cdep)
1
Barrier rule
ID ∝ exp(qψs / kT): the current depends only on the hill height ψs.
2
10× current needs 59.5 mV
Δψs = (kT/q)·ln10 = 25.85 mV × 2.303 = 59.5 mV at 300 K.
3
The gate moves ψs through a divider
Only the part Cox / (Cox + Cdep) of ΔVG reaches ψs.
But the gate does not move ψs one-for-one: it shares its voltage with Cdep.
Notes: Proof in four steps. Gate-all-around brings m close to 1, which is why our devices are near 60 mV/dec.

## Slide 26
The MOSFET – Why SS can never beat 60 mV/dec
Two facts give the limit: the barrier rule and a capacitor divider
gate VG
Cox (gate oxide)
ψs (hill height)
Cdep (depleted body)
body / source
Δψs = ΔVG · Cox / (Cox + Cdep)
1
Barrier rule
ID ∝ exp(qψs / kT): the current depends only on the hill height ψs.
2
10× current needs 59.5 mV
Δψs = (kT/q)·ln10 = 25.85 mV × 2.303 = 59.5 mV at 300 K.
3
The gate moves ψs through a divider
Only the part Cox / (Cox + Cdep) of ΔVG reaches ψs.
4
So SS ≥ 60 mV/dec
SS = 59.5 mV × (1 + Cdep/Cox) = m × 59.5. m ≥ 1, so SS ≥ 59.5 mV/dec.
Ours: standard 61.3 → m = 1.03 · reproduced 65.4 → m = 1.10.
SS = m × 59.5 mV/dec, m = 1 + Cdep/Cox ≥ 1: a better gate makes m closer to 1.
Notes: Proof in four steps. Gate-all-around brings m close to 1, which is why our devices are near 60 mV/dec.

## Slide 27
The MOSFET – SS and temperature
kT/q grows with temperature, so the 60 mV/dec limit grows too
250
300
350
400
450
40
60
80
100
channel temperature T (K)
SS limit (mV/dec)
59.5 mV/dec
SSmin = (kT/q)·ln10 = 0.1984 mV/dec per kelvin
temperature T
300.0 K
SS limit
59.5
leakage Ioff
base
300 K, room temperature: the limit is 59.5 mV/dec.
KNOB: channel temperature T 300 K
300
350
400
A self-heated channel switches more softly: heat raises SS and leakage.
Notes: SS limit = (k T / q) ln 10, which rises 0.1984 mV/dec per kelvin. This links the electrical story to the heat story later.

## Slide 28
The MOSFET – SS and temperature
kT/q grows with temperature, so the 60 mV/dec limit grows too
250
300
350
400
450
40
60
80
100
channel temperature T (K)
SS limit (mV/dec)
68.2 mV/dec
SSmin = (kT/q)·ln10 = 0.1984 mV/dec per kelvin
temperature T
343.6 K ▲
SS limit
68.2 ▲
leakage Ioff
higher ▲
343.6 K is the peak of our reproduced GAAFET: the limit is already 68.2 mV/dec.
KNOB: channel temperature T 343.6 K
300
350
400
A self-heated channel switches more softly: heat raises SS and leakage.
Notes: SS limit = (k T / q) ln 10, which rises 0.1984 mV/dec per kelvin. This links the electrical story to the heat story later.

## Slide 29
The MOSFET – SS and temperature
kT/q grows with temperature, so the 60 mV/dec limit grows too
250
300
350
400
450
40
60
80
100
channel temperature T (K)
SS limit (mV/dec)
79.4 mV/dec
SSmin = (kT/q)·ln10 = 0.1984 mV/dec per kelvin
temperature T
400.0 K ▲
SS limit
79.4 ▲
leakage Ioff
highest ▲
At 400 K the limit is 79.4 mV/dec: a hot channel switches much more softly.
KNOB: channel temperature T 400 K
300
350
400
A self-heated channel switches more softly: heat raises SS and leakage.
Notes: SS limit = (k T / q) ln 10, which rises 0.1984 mV/dec per kelvin. This links the electrical story to the heat story later.

## Slide 30
The MOSFET – Turning the drain
Gate fixed at 0.7 V; now the second knob, VD, goes up step by step
p-type silicon (body)
n+ source
n+ drain
gate
VS = 0
VG = 0.70 V
VD = 0.05 V
electron channel
depletion (no free carriers)
electron energy ↑
0
0.2
0.4
0.6
0 µA
10 µA
20 µA
30 µA
drain voltage VD (V)
ID (linear)
pinch-off
6.2 µA
VD = 0.05 V ID = 6.2 µA
LINEAR: the channel is a resistor
KNOB: drain voltage VD 0.1 V
0.0
0.2
0.4
0.6
0.7
Tiny VD: the channel is even from source to drain; ID grows with VD like a resistor.
Notes: Square-law model with V_G − V_T = 0.45 V and a small channel-length modulation, scaled to I_on = 30 µA at V_D = 0.7 V.

## Slide 31
The MOSFET – Turning the drain
Gate fixed at 0.7 V; now the second knob, VD, goes up step by step
p-type silicon (body)
n+ source
n+ drain
gate
VS = 0
VG = 0.70 V
VD = 0.15 V
electron channel
depletion (no free carriers)
electron energy ↑
0
0.2
0.4
0.6
0 µA
10 µA
20 µA
30 µA
drain voltage VD (V)
ID (linear)
pinch-off
16.4 µA
VD = 0.15 V ID = 16.4 µA
LINEAR: ID rises almost in a straight line
KNOB: drain voltage VD 0.1 V
0.0
0.2
0.4
0.6
0.7
More VD: more current; the channel starts to thin near the drain.
Notes: Square-law model with V_G − V_T = 0.45 V and a small channel-length modulation, scaled to I_on = 30 µA at V_D = 0.7 V.

## Slide 32
The MOSFET – Turning the drain
Gate fixed at 0.7 V; now the second knob, VD, goes up step by step
p-type silicon (body)
n+ source
n+ drain
gate
VS = 0
VG = 0.70 V
VD = 0.30 V
electron channel
depletion (no free carriers)
electron energy ↑
0
0.2
0.4
0.6
0 µA
10 µA
20 µA
30 µA
drain voltage VD (V)
ID (linear)
pinch-off
26.3 µA
VD = 0.30 V ID = 26.3 µA
BENDING: channel thins at the drain end
KNOB: drain voltage VD 0.3 V
0.0
0.2
0.4
0.6
0.7
The drain end of the channel gets thinner, so each extra volt adds less current.
Notes: Square-law model with V_G − V_T = 0.45 V and a small channel-length modulation, scaled to I_on = 30 µA at V_D = 0.7 V.

## Slide 33
The MOSFET – Turning the drain
Gate fixed at 0.7 V; now the second knob, VD, goes up step by step
p-type silicon (body)
n+ source
n+ drain
gate
VS = 0
VG = 0.70 V
VD = 0.45 V
electron channel
depletion (no free carriers)
pinch-off point
electron energy ↑
0
0.2
0.4
0.6
0 µA
10 µA
20 µA
30 µA
drain voltage VD (V)
ID (linear)
pinch-off
29.8 µA
VD = 0.45 V ID = 29.8 µA
PINCH-OFF: VD = VG − VT
KNOB: drain voltage VD 0.5 V
0.0
0.2
0.4
0.6
0.7
At VD = VG − VT the channel thins to zero at the drain end: pinch-off.
Notes: Square-law model with V_G − V_T = 0.45 V and a small channel-length modulation, scaled to I_on = 30 µA at V_D = 0.7 V.

## Slide 34
The MOSFET – Turning the drain
Gate fixed at 0.7 V; now the second knob, VD, goes up step by step
p-type silicon (body)
n+ source
n+ drain
gate
VS = 0
VG = 0.70 V
VD = 0.70 V
electron channel
depletion (no free carriers)
pinch-off point
electron energy ↑
0
0.2
0.4
0.6
0 µA
10 µA
20 µA
30 µA
drain voltage VD (V)
ID (linear)
pinch-off
30.0 µA
VD = 0.70 V ID = 30.0 µA
SATURATION: ID ≈ constant = Ion
KNOB: drain voltage VD 0.7 V
0.0
0.2
0.4
0.6
0.7
Beyond pinch-off ID stays flat: Ion is read here, and so is every heat number in this project.
Notes: Square-law model with V_G − V_T = 0.45 V and a small channel-length modulation, scaled to I_on = 30 µA at V_D = 0.7 V.

## Slide 35
Contents
01
The MOSFET switch
Build it · turn the gate · turn the drain · VT and SS in depth
02
Shrinking the gate
Shorter Lg · DIBL and leakage · the scale length λ
03
FinFET → GAAFET
More gate sides · fin width · wire, sheet, stack · our GAA in numbers
04
The new problem: heat
Oxide traps heat · ΔT = Rth · P · what heat does to every metric
05
Literature and method
Five papers · base paper Chen et al. 2025 · Silvaco Atlas flow
06
Three stages in TCAD
Standard GAAFET · reproduce the paper · optimal design D
07
Conclusion
Gains and limits · the whole story · next steps
Chapter 02
Shrinking the gate
Shorter Lg
DIBL and leakage
the scale length λ
Notes: Chapter 2: what goes wrong when the gate gets short.

## Slide 36
Shrinking the gate – Why shorten Lg
Every new node made the gate shorter: faster, smaller and cheaper chips
~1 µm
1980s
→
~100 nm
2000s
→
~20 nm
2012
→
~14 nm
our device
The catch: a shorter gate also brings source and drain closer together. Below about 20 nm the drain starts to reach under the gate and steal control from it.
Shorter Lg: more speed, but source and drain move closer.
Notes: Typical gate lengths over the generations, not to scale. Our device has L_g = 14 nm.

## Slide 37
Shrinking the gate – Planar MOSFET
Same voltages (VG = 0, VD = 0.7 V); only the knob Lg changes
p-type silicon (body)
n+ source
n+ drain
gate
VS = 0
VG = 0.00 V
VD = 0.70 V
pink = depletion around source and drain
electron energy ↑
long-channel hill top
10
20
30
40
50
60
-0.2
-0.1
0.0
0.1
0.2
0.3
gate length Lg (nm)
threshold voltage VT (V)
VD = 0.05 V
VD = 0.7 V
VT (VD = 0.05 V)
0.25 V
VT (VD = 0.7 V)
0.25 V
DIBL
1 mV/V
KNOB: gate length Lg 60 nm
10
20
30
40
50
60
Long gate: the drain cannot reach the hill top. VT is set by the gate alone.
Notes: Model: ΔV_T = −(1 V + V_D)·exp(−L_g / 2λ), planar λ = 4.37 nm, long-channel V_T = 0.25 V. DIBL is the V_T gap between the two drain voltages divided by 0.65 V.

## Slide 38
Shrinking the gate – Planar MOSFET
Same voltages (VG = 0, VD = 0.7 V); only the knob Lg changes
p-type silicon (body)
n+ source
n+ drain
gate
VS = 0
VG = 0.00 V
VD = 0.70 V
pink = depletion around source and drain
electron energy ↑
long-channel hill top
10
20
30
40
50
60
-0.2
-0.1
0.0
0.1
0.2
0.3
gate length Lg (nm)
threshold voltage VT (V)
VD = 0.05 V
VD = 0.7 V
VT (VD = 0.05 V)
0.24 V ▼
VT (VD = 0.7 V)
0.23 V ▼
DIBL
10 mV/V ▲
KNOB: gate length Lg 40 nm
10
20
30
40
50
60
Shorter: the drain depletion starts to reach under the gate; VT barely moves.
Notes: Model: ΔV_T = −(1 V + V_D)·exp(−L_g / 2λ), planar λ = 4.37 nm, long-channel V_T = 0.25 V. DIBL is the V_T gap between the two drain voltages divided by 0.65 V.

## Slide 39
Shrinking the gate – Planar MOSFET
Same voltages (VG = 0, VD = 0.7 V); only the knob Lg changes
p-type silicon (body)
n+ source
n+ drain
gate
VS = 0
VG = 0.00 V
VD = 0.70 V
pink = depletion around source and drain
electron energy ↑
long-channel hill top
10
20
30
40
50
60
-0.2
-0.1
0.0
0.1
0.2
0.3
gate length Lg (nm)
threshold voltage VT (V)
VD = 0.05 V
VD = 0.7 V
VT (VD = 0.05 V)
0.22 V ▼
VT (VD = 0.7 V)
0.20 V ▼
DIBL
32 mV/V ▲
KNOB: gate length Lg 30 nm
10
20
30
40
50
60
Shorter still: with high VD the hill top sinks a little (DIBL = 32 mV/V).
Notes: Model: ΔV_T = −(1 V + V_D)·exp(−L_g / 2λ), planar λ = 4.37 nm, long-channel V_T = 0.25 V. DIBL is the V_T gap between the two drain voltages divided by 0.65 V.

## Slide 40
Shrinking the gate – Planar MOSFET
Same voltages (VG = 0, VD = 0.7 V); only the knob Lg changes
p-type silicon (body)
n+ source
n+ drain
gate
VS = 0
VG = 0.00 V
VD = 0.70 V
leakage path below the gate
pink = depletion around source and drain
electron energy ↑
long-channel hill top
10
20
30
40
50
60
-0.2
-0.1
0.0
0.1
0.2
0.3
gate length Lg (nm)
threshold voltage VT (V)
VD = 0.05 V
VD = 0.7 V
VT (VD = 0.05 V)
0.14 V ▼
VT (VD = 0.7 V)
0.08 V ▼
DIBL
101 mV/V ▲
KNOB: gate length Lg 20 nm
10
20
30
40
50
60
Source and drain depletions almost touch; VT drops and leakage starts below the gate.
Notes: Model: ΔV_T = −(1 V + V_D)·exp(−L_g / 2λ), planar λ = 4.37 nm, long-channel V_T = 0.25 V. DIBL is the V_T gap between the two drain voltages divided by 0.65 V.

## Slide 41
Shrinking the gate – Planar MOSFET
Same voltages (VG = 0, VD = 0.7 V); only the knob Lg changes
p-type silicon (body)
n+ source
n+ drain
gate
VS = 0
VG = 0.00 V
VD = 0.70 V
leakage path below the gate
pink = depletion around source and drain
electron energy ↑
long-channel hill top
10
20
30
40
50
60
-0.2
-0.1
0.0
0.1
0.2
0.3
gate length Lg (nm)
threshold voltage VT (V)
VD = 0.05 V
VD = 0.7 V
VT (VD = 0.05 V)
0.04 V ▼
VT (VD = 0.7 V)
-0.09 V ▼
DIBL
202 mV/V ▲
KNOB: gate length Lg 14 nm
10
20
30
40
50
60
At 14 nm the depletions meet: VT collapses and current leaks below the gate.
Notes: Model: ΔV_T = −(1 V + V_D)·exp(−L_g / 2λ), planar λ = 4.37 nm, long-channel V_T = 0.25 V. DIBL is the V_T gap between the two drain voltages divided by 0.65 V.

## Slide 42
Shrinking the gate – Short-channel effects
At 14 nm the drain, not the gate, starts to control the channel
p-type silicon (body)
n+ source
n+ drain
gate
VS = 0
VG = 0.00 V
VD = 0.70 V
leakage path below the gate
The gate sits on one side only. Deep below, its field is weak and the drain takes over.
DIBL ▲
drain voltage lowers VT
1 → 202 mV/V
SS ▲
turn-on is softer than 60 mV/dec
≈ 60 → 100 mV/dec
Ioff ▲
leakage below the gate even when off
pA → 241 nA
Planar values from 60 nm to 14 nm, simple λ model.
Three symptoms, one cause: the gate controls the channel from one side only.
Notes: When the channel is short, the drain depletion region reaches toward the source. The drain voltage lowers the barrier the gate is supposed to set, and current leaks below the surface where the gate has little control.

## Slide 43
Shrinking the gate – Proof: the scale length λ
The drain potential fades into the channel as e^(−x/λ); more gate sides → smaller λ
silicon
8 nm
planar (1 side)
0
2
4
6
8
10
12
14
0 %
25 %
50 %
75 %
100 %
distance from the drain into the channel x (nm)
drain pull left e^(−x/λ)
4.06 %
λ = √( εsi · tsi · tox / (N · εox) )
N = gate sides · εsi/εox = 3
tsi = 8 nm, tox = EOT 0.8 nm
scale length λ
4.37 nm
Lg / λ at 14 nm
3.2
drain pull at source end
4.06 %
KNOB: gate sides N 1
1
2
3
4
Planar: λ = 4.37 nm; 4 % of the drain pull still reaches the source end of a 14 nm gate.
Notes: Same 8 nm silicon and 0.8 nm EOT for all four. EOT = 0.6 nm SiO2 + 1.1 nm HfO2 × 3.9/22 = 0.8 nm. Each extra gate side drains away the drain field, so it dies faster.

## Slide 44
Shrinking the gate – Proof: the scale length λ
The drain potential fades into the channel as e^(−x/λ); more gate sides → smaller λ
silicon
8 nm
double gate (2 sides)
0
2
4
6
8
10
12
14
0 %
25 %
50 %
75 %
100 %
distance from the drain into the channel x (nm)
drain pull left e^(−x/λ)
1.08 %
λ = √( εsi · tsi · tox / (N · εox) )
N = gate sides · εsi/εox = 3
tsi = 8 nm, tox = EOT 0.8 nm
scale length λ
3.09 nm ▼
Lg / λ at 14 nm
4.5 ▲
drain pull at source end
1.08 % ▼
KNOB: gate sides N 2
1
2
3
4
Two gate sides: λ = 3.09 nm, the pull drops to 1 %.
Notes: Same 8 nm silicon and 0.8 nm EOT for all four. EOT = 0.6 nm SiO2 + 1.1 nm HfO2 × 3.9/22 = 0.8 nm. Each extra gate side drains away the drain field, so it dies faster.

## Slide 45
Shrinking the gate – Proof: the scale length λ
The drain potential fades into the channel as e^(−x/λ); more gate sides → smaller λ
silicon
8 nm
FinFET (3 sides)
0
2
4
6
8
10
12
14
0 %
25 %
50 %
75 %
100 %
distance from the drain into the channel x (nm)
drain pull left e^(−x/λ)
0.39 %
λ = √( εsi · tsi · tox / (N · εox) )
N = gate sides · εsi/εox = 3
tsi = 8 nm, tox = EOT 0.8 nm
scale length λ
2.52 nm ▼
Lg / λ at 14 nm
5.6 ▲
drain pull at source end
0.39 % ▼
KNOB: gate sides N 3
1
2
3
4
FinFET, three sides: λ = 2.52 nm, 0.39 %.
Notes: Same 8 nm silicon and 0.8 nm EOT for all four. EOT = 0.6 nm SiO2 + 1.1 nm HfO2 × 3.9/22 = 0.8 nm. Each extra gate side drains away the drain field, so it dies faster.

## Slide 46
Shrinking the gate – Proof: the scale length λ
The drain potential fades into the channel as e^(−x/λ); more gate sides → smaller λ
silicon
8 nm
gate-all-around (4)
0
2
4
6
8
10
12
14
0 %
25 %
50 %
75 %
100 %
distance from the drain into the channel x (nm)
drain pull left e^(−x/λ)
0.16 %
λ = √( εsi · tsi · tox / (N · εox) )
N = gate sides · εsi/εox = 3
tsi = 8 nm, tox = EOT 0.8 nm
scale length λ
2.18 nm ▼
Lg / λ at 14 nm
6.4 ▲
drain pull at source end
0.16 % ▼
KNOB: gate sides N 4
1
2
3
4
Gate-all-around: λ = 2.18 nm, only 0.16 %. The gate needs Lg ≥ 5–10 λ to stay in control.
Notes: Same 8 nm silicon and 0.8 nm EOT for all four. EOT = 0.6 nm SiO2 + 1.1 nm HfO2 × 3.9/22 = 0.8 nm. Each extra gate side drains away the drain field, so it dies faster.

## Slide 47
Contents
01
The MOSFET switch
Build it · turn the gate · turn the drain · VT and SS in depth
02
Shrinking the gate
Shorter Lg · DIBL and leakage · the scale length λ
03
FinFET → GAAFET
More gate sides · fin width · wire, sheet, stack · our GAA in numbers
04
The new problem: heat
Oxide traps heat · ΔT = Rth · P · what heat does to every metric
05
Literature and method
Five papers · base paper Chen et al. 2025 · Silvaco Atlas flow
06
Three stages in TCAD
Standard GAAFET · reproduce the paper · optimal design D
07
Conclusion
Gains and limits · the whole story · next steps
Chapter 03
FinFET → GAAFET
More gate sides
fin width
wire, sheet, stack
our GAA in numbers
Notes: Chapter 3: wrap more gate around the channel.

## Slide 48
From planar to GAA – One camera, four transistors
Looking along the channel: current flows into the screen
silicon substrate
gate on top only
leakage deep below the gate
1
Planar: gate on top only
The gate touches the channel from one side. Deep below, its field is weak, so at short Lg electrons leak there.
gate sides N
1
λ
4.37 nm
DIBL at 14 nm
201 mV/V
SS at 14 nm: 100 mV/dec (simple λ model, same 8 nm silicon)
A flat channel: the gate controls only its top surface.
Notes: The gate touches the channel from one side. Deep below, its field is weak, so at short L_g electrons leak there.

## Slide 49
From planar to GAA – One camera, four transistors
Looking along the channel: current flows into the screen
silicon substrate
isolation oxide
gate on top only
2
Stand the channel up: a fin
Make the channel a thin, tall wall of silicon. Source and drain are the two ends of the fin (in and out of the screen).
gate sides N
1
λ
4.37 nm
DIBL at 14 nm
201 mV/V
SS at 14 nm: 100 mV/dec (simple λ model, same 8 nm silicon)
The channel stands up into a vertical fin.
Notes: Make the channel a thin, tall wall of silicon. Source and drain are the two ends of the fin (in and out of the screen).

## Slide 50
From planar to GAA – One camera, four transistors
Looking along the channel: current flows into the screen
silicon substrate
isolation oxide
gate wraps 3 sides
3
Wrap the gate over it
The gate now covers the left, top and right of the fin, like a saddle over a wall. The fin is thin, so no point is far from the gate.
gate sides N
3 ▲
λ
2.52 nm ▼
DIBL at 14 nm
62 mV/V ▼
SS at 14 nm: 68 mV/dec (simple λ model, same 8 nm silicon)
The gate wraps the fin on three sides: λ falls from 4.37 to 2.52 nm.
Notes: The gate now covers the left, top and right of the fin, like a saddle over a wall. The fin is thin, so no point is far from the gate.

## Slide 51
From planar to GAA – One camera, four transistors
Looking along the channel: current flows into the screen
silicon substrate
isolation oxide
gate wraps 3 sides
4
Channel on three surfaces
Above VT electrons gather on the top and both sides at once. Taller fin = more surface = more current.
gate sides N
3
λ
2.52 nm
DIBL at 14 nm
62 mV/V
SS at 14 nm: 68 mV/dec (simple λ model, same 8 nm silicon)
The channel forms on three surfaces at once.
Notes: Above V_T electrons gather on the top and both sides at once. Taller fin = more surface = more current.

## Slide 52
From planar to GAA – One camera, four transistors
Looking along the channel: current flows into the screen
silicon substrate
isolation oxide
gate wraps 3 sides
bottom: no gate here
5
But the bottom is open
The fin bottom sits in the substrate with no gate there: some leakage remains. Fix: cut the channel free from the substrate.
gate sides N
3
λ
2.52 nm
DIBL at 14 nm
62 mV/V
SS at 14 nm: 68 mV/dec (simple λ model, same 8 nm silicon)
The open bottom is the FinFET's weak spot.
Notes: The fin bottom sits in the substrate with no gate there: some leakage remains. Fix: cut the channel free from the substrate.

## Slide 53
From planar to GAA – One camera, four transistors
Looking along the channel: current flows into the screen
silicon substrate
isolation oxide
metal gate (all round)
6
Cut it free: gate-all-around
The channel becomes a sheet hanging inside the gate. The gate surrounds it: top, bottom, left and right. No open side, no leakage path.
gate sides N
4 ▲
λ
2.18 nm ▼
DIBL at 14 nm
41 mV/V ▼
SS at 14 nm: 65 mV/dec (simple λ model, same 8 nm silicon)
Gate-all-around: the best electrostatic control, used at 3 nm and below.
Notes: The channel becomes a sheet hanging inside the gate. The gate surrounds it: top, bottom, left and right. No open side, no leakage path.

## Slide 54
From planar to GAA – One camera, four transistors
Looking along the channel: current flows into the screen
silicon substrate
isolation oxide
metal gate (all round)
7
Stack the sheets
Three sheets under one gate: 3× the current in the same footprint, with the same gate control. This is the 3 nm-class transistor.
gate sides N
4
λ
2.18 nm
DIBL at 14 nm
41 mV/V
SS at 14 nm: 65 mV/dec (simple λ model, same 8 nm silicon)
Stacked sheets: more current per footprint, same control.
Notes: Three sheets under one gate: 3× the current in the same footprint, with the same gate control. This is the 3 nm-class transistor.

## Slide 55
FinFET – The fin width knob
Thinner fin: every point is closer to the gate, so λ and leakage fall
Wfin = 12 nm
Hfin = 40 nm
4
6
8
10
12
0.00
0.04
0.08
0.12
fin width Wfin (nm)
short-channel effect at Lg = 14 nm
scale length λ
3.10 nm
SCE = e^(−L/2λ)
0.104
Weff = 2H + W
92 nm
KNOB: fin width Wfin 12 nm
4
6
8
10
12
Wide fin (12 nm): the centre is far from the gate; control is only fair.
Notes: λ = √(3 · W_fin · 0.8 nm / 3); SCE = exp(−L_g / 2λ). Thinner fins help control but cost width and are hard to etch.

## Slide 56
FinFET – The fin width knob
Thinner fin: every point is closer to the gate, so λ and leakage fall
Wfin = 8 nm
Hfin = 40 nm
4
6
8
10
12
0.00
0.04
0.08
0.12
fin width Wfin (nm)
short-channel effect at Lg = 14 nm
scale length λ
2.53 nm ▼
SCE = e^(−L/2λ)
0.063 ▼
Weff = 2H + W
88 nm ▼
KNOB: fin width Wfin 8 nm
4
6
8
10
12
Fin 8 nm: three gate sides give λ = 2.52 nm, far better than planar (4.37 nm).
Notes: λ = √(3 · W_fin · 0.8 nm / 3); SCE = exp(−L_g / 2λ). Thinner fins help control but cost width and are hard to etch.

## Slide 57
FinFET – The fin width knob
Thinner fin: every point is closer to the gate, so λ and leakage fall
Wfin = 5 nm
Hfin = 40 nm
4
6
8
10
12
0.00
0.04
0.08
0.12
fin width Wfin (nm)
short-channel effect at Lg = 14 nm
scale length λ
2.00 nm ▼
SCE = e^(−L/2λ)
0.030 ▼
Weff = 2H + W
85 nm ▼
KNOB: fin width Wfin 5 nm
4
6
8
10
12
Thin fin (5 nm): λ = 2.0 nm, but the fin is hard to make and carries a little less current.
Notes: λ = √(3 · W_fin · 0.8 nm / 3); SCE = exp(−L_g / 2λ). Thinner fins help control but cost width and are hard to etch.

## Slide 58
GAAFET – Wire, sheet, stack
The shape of the channel sets the current (Weff) and the control (λ)
Nanowire, r = 4 nm
our standard device
gate (all round)
Weff = gate perimeter (nm) → Ion ∝ Weff
25.1
wire 4
wire 5.64
sheet
stack
Weff
25.1 nm
scale length λ
2.18 nm
silicon area
50 nm²
A round wire: gate on every side, nothing is far from the gate.
Notes: Weff is the perimeter the gate wraps: 2πr for a wire, 2(W+T) for a sheet, times the number of sheets.

## Slide 59
GAAFET – Wire, sheet, stack
The shape of the channel sets the current (Weff) and the control (λ)
Nanowire, r = 5.64 nm
our reproduced device (same 100 nm² as the sheet)
gate (all round)
Weff = gate perimeter (nm) → Ion ∝ Weff
25.1
wire 4
35.4
wire 5.64
sheet
stack
Weff
35.4 nm ▲
scale length λ
2.59 nm ▲
silicon area
100 nm² ▲
Thicker wire: more current, but the centre is farther from the gate (λ up).
Notes: Weff is the perimeter the gate wraps: 2πr for a wire, 2(W+T) for a sheet, times the number of sheets.

## Slide 60
GAAFET – Wire, sheet, stack
The shape of the channel sets the current (Weff) and the control (λ)
Nanosheet, 20 × 5 nm
base paper [1]
gate (all round)
Weff = gate perimeter (nm) → Ion ∝ Weff
25.1
wire 4
35.4
wire 5.64
50.0
sheet
stack
Weff
50.0 nm ▲
scale length λ
1.73 nm ▼
silicon area
100 nm²
A flat sheet: thin (5 nm) for control, wide (20 nm) for more current.
Notes: Weff is the perimeter the gate wraps: 2πr for a wire, 2(W+T) for a sheet, times the number of sheets.

## Slide 61
GAAFET – Wire, sheet, stack
The shape of the channel sets the current (Weff) and the control (λ)
3 stacked sheets
3 nm-class chips
gate (all round)
Weff = gate perimeter (nm) → Ion ∝ Weff
25.1
wire 4
35.4
wire 5.64
50.0
sheet
150.0
stack
Weff
150.0 nm ▲
scale length λ
1.73 nm
silicon area
300 nm² ▲
Stack three sheets: 3× the current in the same footprint, same gate control.
Notes: Weff is the perimeter the gate wraps: 2πr for a wire, 2(W+T) for a sheet, times the number of sheets.

## Slide 62
GAAFET – How it is made
Side view along the channel: from a layer cake to sheets wrapped by the gate
silicon sheets (yellow)
SiGe, removed later (grey)
1
Grow a layer cake
Alternate silicon (yellow) and SiGe (grey) layers, then etch them into one wide fin.
GAA starts as a fin made of alternating layers.
Notes: Alternate silicon (yellow) and SiGe (grey) layers, then etch them into one wide fin.

## Slide 63
GAAFET – How it is made
Side view along the channel: from a layer cake to sheets wrapped by the gate
dummy gate
silicon sheets (yellow)
SiGe, removed later (grey)
2
Place a dummy gate
A temporary gate and nitride spacers mark where the real gate will go.
A placeholder gate holds the shape.
Notes: A temporary gate and nitride spacers mark where the real gate will go.

## Slide 64
GAAFET – How it is made
Side view along the channel: from a layer cake to sheets wrapped by the gate
dummy gate
n+ source
n+ drain
silicon sheets (yellow)
SiGe, removed later (grey)
3
Grow source and drain
The fin ends are replaced by n+ silicon. They clamp the silicon sheets at both ends.
Source and drain hold the silicon sheets.
Notes: The fin ends are replaced by n+ silicon. They clamp the silicon sheets at both ends.

## Slide 65
GAAFET – How it is made
Side view along the channel: from a layer cake to sheets wrapped by the gate
(removed)
n+ source
n+ drain
silicon sheets (yellow)
gaps where SiGe was
4
Remove dummy gate and SiGe
A selective etch removes only the SiGe. The silicon sheets now hang like bridges.
The sheets are free: there is space all around them.
Notes: A selective etch removes only the SiGe. The silicon sheets now hang like bridges.

## Slide 66
GAAFET – How it is made
Side view along the channel: from a layer cake to sheets wrapped by the gate
metal gate
n+ source
n+ drain
silicon sheets (yellow)
gate fills the gaps (lavender)
5
Fill with gate all around
HfO2, then metal, fill every gap. Each sheet is wrapped on all four sides.
The gate now surrounds every sheet.
Notes: HfO2, then metal, fill every gap. Each sheet is wrapped on all four sides.

## Slide 67
GAAFET – Turning the gate in our wire
Reproduced GAA wire (r = 5.64 nm, Lg = 14 nm): Silvaco Atlas data, VD = 0.7 V
wire cross-section (gate all round)
gate
HfO2 / SiO2
silicon
electrons
0
0.2
0.4
0.6
100 pA
10 nA
1 µA
100 µA
gate voltage VG (V)
ID (log)
planar at 14 nm
624 pA
VG = 0.00 V ID = 624 pA
OFF: Ioff = 624 pA
KNOB: gate voltage VG 0.0 V
0.0
0.2
0.4
0.6
0.7
VG = 0: the gate holds the hill high all round the wire. Leakage: 624 pA.
Notes: Green: Atlas, our reproduced GAAFET at V_D = 0.7 V. Dashed grey: the planar model at the same 14 nm gate length.

## Slide 68
GAAFET – Turning the gate in our wire
Reproduced GAA wire (r = 5.64 nm, Lg = 14 nm): Silvaco Atlas data, VD = 0.7 V
wire cross-section (gate all round)
gate
HfO2 / SiO2
silicon
electrons
0
0.2
0.4
0.6
100 pA
10 nA
1 µA
100 µA
gate voltage VG (V)
ID (log)
planar at 14 nm
18 nA
VG = 0.10 V ID = 18 nA
SUBTHRESHOLD
KNOB: gate voltage VG 0.1 V
0.0
0.2
0.4
0.6
0.7
Gate up: the whole surface of the wire pulls the hill down together.
Notes: Green: Atlas, our reproduced GAAFET at V_D = 0.7 V. Dashed grey: the planar model at the same 14 nm gate length.

## Slide 69
GAAFET – Turning the gate in our wire
Reproduced GAA wire (r = 5.64 nm, Lg = 14 nm): Silvaco Atlas data, VD = 0.7 V
wire cross-section (gate all round)
gate
HfO2 / SiO2
silicon
electrons
0
0.2
0.4
0.6
100 pA
10 nA
1 µA
100 µA
gate voltage VG (V)
ID (log)
planar at 14 nm
453 nA
VG = 0.20 V ID = 453 nA
NEAR VT = 0.204 V
KNOB: gate voltage VG 0.2 V
0.0
0.2
0.4
0.6
0.7
Near VT a thin ring of electrons forms just inside the oxide.
Notes: Green: Atlas, our reproduced GAAFET at V_D = 0.7 V. Dashed grey: the planar model at the same 14 nm gate length.

## Slide 70
GAAFET – Turning the gate in our wire
Reproduced GAA wire (r = 5.64 nm, Lg = 14 nm): Silvaco Atlas data, VD = 0.7 V
wire cross-section (gate all round)
gate
HfO2 / SiO2
silicon
electrons
0
0.2
0.4
0.6
100 pA
10 nA
1 µA
100 µA
gate voltage VG (V)
ID (log)
planar at 14 nm
3.6 µA
VG = 0.30 V ID = 3.6 µA
CHANNEL FORMED: a ring
KNOB: gate voltage VG 0.3 V
0.0
0.2
0.4
0.6
0.7
Past VT the electron ring thickens all round the wire.
Notes: Green: Atlas, our reproduced GAAFET at V_D = 0.7 V. Dashed grey: the planar model at the same 14 nm gate length.

## Slide 71
GAAFET – Turning the gate in our wire
Reproduced GAA wire (r = 5.64 nm, Lg = 14 nm): Silvaco Atlas data, VD = 0.7 V
wire cross-section (gate all round)
gate
HfO2 / SiO2
silicon
electrons
0
0.2
0.4
0.6
100 pA
10 nA
1 µA
100 µA
gate voltage VG (V)
ID (log)
planar at 14 nm
13.9 µA
VG = 0.50 V ID = 13.9 µA
STRONG INVERSION
KNOB: gate voltage VG 0.5 V
0.0
0.2
0.4
0.6
0.7
The ring grows inward: most of the wire now carries current.
Notes: Green: Atlas, our reproduced GAAFET at V_D = 0.7 V. Dashed grey: the planar model at the same 14 nm gate length.

## Slide 72
GAAFET – Turning the gate in our wire
Reproduced GAA wire (r = 5.64 nm, Lg = 14 nm): Silvaco Atlas data, VD = 0.7 V
wire cross-section (gate all round)
gate
HfO2 / SiO2
silicon
electrons
0
0.2
0.4
0.6
100 pA
10 nA
1 µA
100 µA
gate voltage VG (V)
ID (log)
planar at 14 nm
27.5 µA
VG = 0.70 V ID = 27.5 µA
ON: Ion = 27.5 µA
KNOB: gate voltage VG 0.7 V
0.0
0.2
0.4
0.6
0.7
VG = 0.7 V: the whole wire conducts (volume inversion): Ion = 27.5 µA.
Notes: Green: Atlas, our reproduced GAAFET at V_D = 0.7 V. Dashed grey: the planar model at the same 14 nm gate length.

## Slide 73
Planar vs FinFET vs GAA
Same 14 nm gate, same silicon: only the number of gate sides changes
0
0.1
0.2
0.3
0.4
0.5
0.6
0.7
10 pA
1 nA
100 nA
10 µA
gate voltage VG (V)
ID at VD = 0.7 V (log)
planar (1 side)
Ioff = 241 nA
λ = 4.37 nm · SS ≈ 100 mV/dec · DIBL ≈ 201 mV/V · VT = 0.01 V
FinFET (3 sides)
GAA (all round)
Planar at 14 nm: soft turn-on and 241 nA of leakage.
Notes: Simple λ model, same width, long-channel V_T = 0.35 V: SS = 59.5/(1 − 2e^(−L/2λ)), ΔV_T = 1.7·e^(−L/2λ). For learning, not Atlas data.

## Slide 74
Planar vs FinFET vs GAA
Same 14 nm gate, same silicon: only the number of gate sides changes
0
0.1
0.2
0.3
0.4
0.5
0.6
0.7
10 pA
1 nA
100 nA
10 µA
gate voltage VG (V)
ID at VD = 0.7 V (log)
planar (1 side)
Ioff = 241 nA
λ = 4.37 nm · SS ≈ 100 mV/dec · DIBL ≈ 201 mV/V · VT = 0.01 V
FinFET (3 sides)
Ioff = 144 pA
λ = 2.52 nm · SS ≈ 68 mV/dec · DIBL ≈ 62 mV/V · VT = 0.24 V
GAA (all round)
FinFET: steeper turn-on, VT kept, leakage down about 1700×.
Notes: Simple λ model, same width, long-channel V_T = 0.35 V: SS = 59.5/(1 − 2e^(−L/2λ)), ΔV_T = 1.7·e^(−L/2λ). For learning, not Atlas data.

## Slide 75
Planar vs FinFET vs GAA
Same 14 nm gate, same silicon: only the number of gate sides changes
0
0.1
0.2
0.3
0.4
0.5
0.6
0.7
10 pA
1 nA
100 nA
10 µA
gate voltage VG (V)
ID at VD = 0.7 V (log)
planar (1 side)
Ioff = 241 nA
λ = 4.37 nm · SS ≈ 100 mV/dec · DIBL ≈ 201 mV/V · VT = 0.01 V
FinFET (3 sides)
Ioff = 144 pA
λ = 2.52 nm · SS ≈ 68 mV/dec · DIBL ≈ 62 mV/V · VT = 0.24 V
GAA (all round)
Ioff = 26 pA
λ = 2.18 nm · SS ≈ 65 mV/dec · DIBL ≈ 41 mV/V · VT = 0.28 V
GAA: steepest turn-on and about 10 000× less leakage than planar.
Notes: Simple λ model, same width, long-channel V_T = 0.35 V: SS = 59.5/(1 − 2e^(−L/2λ)), ΔV_T = 1.7·e^(−L/2λ). For learning, not Atlas data.

## Slide 76
Why gate-all-around wins at 14 nm
Lg / λ for a 14 nm gate: the gate stays in control when Lg ≥ 5–10 λ
good zone: Lg ≥ 5 λ
3.2
planar
λ = 4.37 nm
4.5
double gate
λ = 3.09 nm
5.6
FinFET
λ = 2.52 nm
6.4
GAA
λ = 2.18 nm
Reading the bars
λ = √(3 · 8 nm · 0.8 nm / N).
More sides N → smaller λ → the gate wins over the drain.
Planar 3.2 and double gate 4.5 fail at 14 nm.
FinFET 5.6 just passes; GAA 6.4 is safest.
A real fin has an open bottom, so a real FinFET is a bit worse than N = 3.
Only GAA keeps Lg / λ above 6 at Lg = 14 nm: that is why 3 nm-class chips use it.
Notes: Lg over lambda for a 14 nm gate, for one to four gate sides.

## Slide 77
GAAFET – Measuring DIBL on our data
Raise VD from 0.05 V to 0.7 V: the whole curve shifts left
0
0.1
0.2
0.3
0.4
0.5
0.6
0.7
100 pA
10 nA
1 µA
100 µA
gate voltage VG (V)
ID (log)
VD = 0.05 V
VD = 0.7 V
Two drain voltages
Same device, two transfer curves: VD = 0.05 V and 0.7 V.
DIBL = shift ÷ ΔVD: a small number means the gate, not the drain, is in charge.
Notes: Constant-current method at 10 nA on the Atlas curves of the reproduced GAAFET.

## Slide 78
GAAFET – Measuring DIBL on our data
Raise VD from 0.05 V to 0.7 V: the whole curve shifts left
0
0.1
0.2
0.3
0.4
0.5
0.6
0.7
100 pA
10 nA
1 µA
100 µA
gate voltage VG (V)
ID (log)
VD = 0.05 V
VD = 0.7 V
I = 10 nA
Two drain voltages
Same device, two transfer curves: VD = 0.05 V and 0.7 V.
Pick one current
Draw a line at 10 nA and read where each curve crosses it.
DIBL = shift ÷ ΔVD: a small number means the gate, not the drain, is in charge.
Notes: Constant-current method at 10 nA on the Atlas curves of the reproduced GAAFET.

## Slide 79
GAAFET – Measuring DIBL on our data
Raise VD from 0.05 V to 0.7 V: the whole curve shifts left
0
0.1
0.2
0.3
0.4
0.5
0.6
0.7
100 pA
10 nA
1 µA
100 µA
gate voltage VG (V)
ID (log)
VD = 0.05 V
VD = 0.7 V
I = 10 nA
24.4 mV
Two drain voltages
Same device, two transfer curves: VD = 0.05 V and 0.7 V.
Pick one current
Draw a line at 10 nA and read where each curve crosses it.
Read the shift
VG needed: 0.107 V → 0.083 V, a shift of 24.4 mV.
DIBL = 24.4 mV / 0.65 V = 38 mV/V.
Standard wire r = 4 nm: 17.3 mV/V · reproduced r = 5.64 nm: 38 mV/V.
Thicker wire → weaker gate grip.
DIBL = shift ÷ ΔVD: a small number means the gate, not the drain, is in charge.
Notes: Constant-current method at 10 nA on the Atlas curves of the reproduced GAAFET.

## Slide 80
Our GAA device in numbers
Standard cylindrical GAAFET in Atlas (Lg = 14 nm, r = 4 nm), before any thermal tuning
61.3 mV/dec
subthreshold swing
ideal limit 60
17.3 mV/V
DIBL
drain barely moves VT
99 pA
Ioff
tiny leakage when off
1.8×10⁵
Ion / Ioff
clean switch
Metric | Our standard GAA | Gets better when
VT | 0.209 V | φm ↑ raises it; short Lg lowers it
SS | 61.3 mV/dec | more gate sides, thin oxide, cooler
DIBL | 17.3 mV/V | large Lg / λ (GAA, thin wire)
Ion | 17.9 µA | Weff ↑, VT ↓, cooler (μ ↑)
Ioff | 99 pA | VT ↑, SS ↓, DIBL ↓
λ | 2.18 nm | N ↑, tsi ↓, tox ↓
GAA solves the short-channel problem at Lg = 14 nm.
Notes: Electrical results of our standard cylindrical GAAFET in Atlas, before any thermal tuning. Subthreshold swing is close to the 60 mV/dec limit and DIBL is small.

## Slide 81
Contents
01
The MOSFET switch
Build it · turn the gate · turn the drain · VT and SS in depth
02
Shrinking the gate
Shorter Lg · DIBL and leakage · the scale length λ
03
FinFET → GAAFET
More gate sides · fin width · wire, sheet, stack · our GAA in numbers
04
The new problem: heat
Oxide traps heat · ΔT = Rth · P · what heat does to every metric
05
Literature and method
Five papers · base paper Chen et al. 2025 · Silvaco Atlas flow
06
Three stages in TCAD
Standard GAAFET · reproduce the paper · optimal design D
07
Conclusion
Gains and limits · the whole story · next steps
Chapter 04
The new problem: heat
Oxide traps heat
ΔT = Rth
P
what heat does to every metric
Notes: Chapter 4: the price of gate-all-around is heat.

## Slide 82
The new problem – The oxide traps the heat
Thermal conductivity κ of every material around our channel (W/m·K, log scale)
Chart: 
| Si substrate | Si channel | Si₃N₄ spacer | HfO₂ | SiO₂
κ | 148 | 22 | 18 | 2.3 | 1.4
10–100×
worse heat conduction in the oxides that wrap the GAA channel
Joule heat P = ID · VDS
every working transistor turns its power into heat
The gate oxide is what gives GAA its control. It is also what keeps the heat in.
Better gate control comes with a worse heat path.
Notes: Current through the channel makes Joule heat. In GAA the channel is surrounded by SiO2 and HfO2, which conduct heat ten to a hundred times worse than silicon, so the heat has no easy way out.

## Slide 83
The new problem – Ohm's law for heat
Heat flows like current through a chain of thermal resistances
P
heat source
(channel)
Roxide
SiO2 + HfO2
Rgate
metal shell
Rcontact
contacts, wires
300 K
heat sink
Electrical | Thermal
voltage V | temperature rise ΔT (K)
current I | power P (W)
resistance R | thermal resistance Rth (K/W)
V = I · R | ΔT = P · Rth
Base paper target
64.8 K
at 30 µW
Rth = 2.16 × 10⁶ K/W
Our job: build a device with the same Rth, then lower it.
ΔT = Rth · P: lower Rth or lower P to run cooler.
Notes: Heat flow behaves like current in a resistor network. The temperature rise equals thermal resistance times power. Each low-conductivity layer adds resistance.

## Slide 84
Self-heating – What happens inside
Same GAA wire, now running at VG = VD = 0.7 V (side view along the channel)
source
drain
gate (wraps)
300 K
300 K
300 K
hot spot: drain end
1
Current makes heat
Moving electrons carry power P = ID · VD. That power must turn into heat somewhere.
Every working transistor turns its power into heat.
Notes: Moving electrons carry power P = I_D · V_D. That power must turn into heat somewhere.

## Slide 85
Self-heating – What happens inside
Same GAA wire, now running at VG = VD = 0.7 V (side view along the channel)
source
drain
gate (wraps)
300 K
300 K
300 K
hot spot: drain end
2
Hot spot at the drain end
Near the drain the field is strongest. Fast electrons hit the silicon atoms there and the crystal vibrates: it heats up.
The hot spot forms at the drain end of the wire.
Notes: Near the drain the field is strongest. Fast electrons hit the silicon atoms there and the crystal vibrates: it heats up.

## Slide 86
Self-heating – What happens inside
Same GAA wire, now running at VG = VD = 0.7 V (side view along the channel)
source
drain
gate (wraps)
300 K
300 K
300 K
heat trapped by the oxide
hot spot: drain end
3
The oxide traps the heat
The wire is wrapped in SiO₂ and HfO₂, which conduct heat 10–100× worse than silicon. Heat cannot get out easily.
Good for gate control, bad for cooling.
Notes: The wire is wrapped in SiO₂ and HfO₂, which conduct heat 10–100× worse than silicon. Heat cannot get out easily.

## Slide 87
Self-heating – What happens inside
Same GAA wire, now running at VG = VD = 0.7 V (side view along the channel)
source
drain
gate (wraps)
300 K
300 K
300 K
heat trapped by the oxide
hot spot: drain end
4
Heat escapes through metal
It leaves through the drain, the gate metal and the contacts to 300 K. A harder path means a hotter channel: ΔT = Rth · P.
Better heat paths (lower Rth) keep the channel cool: that is our project.
Notes: It leaves through the drain, the gate metal and the contacts to 300 K. A harder path means a hotter channel: ΔT = R_th · P.

## Slide 88
Self-heating – Where the heat goes
Reproduced GAAFET, VD = 0.7 V, VG raised step by step (Silvaco Atlas)
source
drain
gate (wraps)
300 K
300 K
300 K
hot spot: drain end
0
5
10
15
20
0
10
20
30
40
50
power P = ID·VD (µW)
temperature rise ΔT (K)
1.0 K
power P
0.3 µW
rise ΔT
1.0 K
Rth = ΔT / P
3.19 K/µW
KNOB: gate voltage VG 0.2 V
0.0
0.2
0.4
0.6
0.7
VG = 0.2 V: almost no current, almost no heat: the wire stays near 300 K.
Notes: Each point is one gate voltage of the V_D = 0.7 V Atlas sweep, plotted as temperature rise against dissipated power. At the on point R_th = 2.27 × 10⁶ K/W.

## Slide 89
Self-heating – Where the heat goes
Reproduced GAAFET, VD = 0.7 V, VG raised step by step (Silvaco Atlas)
source
drain
gate (wraps)
300 K
300 K
300 K
hot spot: drain end
0
5
10
15
20
0
10
20
30
40
50
power P = ID·VD (µW)
temperature rise ΔT (K)
7.4 K
power P
2.5 µW ▲
rise ΔT
7.4 K ▲
Rth = ΔT / P
2.92 K/µW
KNOB: gate voltage VG 0.3 V
0.0
0.2
0.4
0.6
0.7
Low power: a little Joule heat appears at the drain end.
Notes: Each point is one gate voltage of the V_D = 0.7 V Atlas sweep, plotted as temperature rise against dissipated power. At the on point R_th = 2.27 × 10⁶ K/W.

## Slide 90
Self-heating – Where the heat goes
Reproduced GAAFET, VD = 0.7 V, VG raised step by step (Silvaco Atlas)
source
drain
gate (wraps)
300 K
300 K
300 K
hot spot: drain end
0
5
10
15
20
0
10
20
30
40
50
power P = ID·VD (µW)
temperature rise ΔT (K)
15.5 K
power P
5.7 µW ▲
rise ΔT
15.5 K ▲
Rth = ΔT / P
2.70 K/µW
KNOB: gate voltage VG 0.4 V
0.0
0.2
0.4
0.6
0.7
Current rises: heat grows and collects where the field is strongest.
Notes: Each point is one gate voltage of the V_D = 0.7 V Atlas sweep, plotted as temperature rise against dissipated power. At the on point R_th = 2.27 × 10⁶ K/W.

## Slide 91
Self-heating – Where the heat goes
Reproduced GAAFET, VD = 0.7 V, VG raised step by step (Silvaco Atlas)
source
drain
gate (wraps)
300 K
300 K
300 K
hot spot: drain end
0
5
10
15
20
0
10
20
30
40
50
power P = ID·VD (µW)
temperature rise ΔT (K)
24.7 K
power P
9.8 µW ▲
rise ΔT
24.7 K ▲
Rth = ΔT / P
2.53 K/µW
KNOB: gate voltage VG 0.5 V
0.0
0.2
0.4
0.6
0.7
More current, more heat: the oxide around the wire holds it in.
Notes: Each point is one gate voltage of the V_D = 0.7 V Atlas sweep, plotted as temperature rise against dissipated power. At the on point R_th = 2.27 × 10⁶ K/W.

## Slide 92
Self-heating – Where the heat goes
Reproduced GAAFET, VD = 0.7 V, VG raised step by step (Silvaco Atlas)
source
drain
gate (wraps)
300 K
300 K
300 K
hot spot: drain end
0
5
10
15
20
0
10
20
30
40
50
power P = ID·VD (µW)
temperature rise ΔT (K)
34.2 K
power P
14.3 µW ▲
rise ΔT
34.2 K ▲
Rth = ΔT / P
2.39 K/µW
KNOB: gate voltage VG 0.6 V
0.0
0.2
0.4
0.6
0.7
Heat now flows out through the contacts and the gate metal.
Notes: Each point is one gate voltage of the V_D = 0.7 V Atlas sweep, plotted as temperature rise against dissipated power. At the on point R_th = 2.27 × 10⁶ K/W.

## Slide 93
Self-heating – Where the heat goes
Reproduced GAAFET, VD = 0.7 V, VG raised step by step (Silvaco Atlas)
source
drain
gate (wraps)
300 K
300 K
300 K
hot spot: drain end
0
5
10
15
20
0
10
20
30
40
50
power P = ID·VD (µW)
temperature rise ΔT (K)
43.6 K
power P
19.2 µW ▲
rise ΔT
43.6 K ▲
Rth = ΔT / P
2.27 K/µW
KNOB: gate voltage VG 0.7 V
0.0
0.2
0.4
0.6
0.7
On point: 19.2 µW → 43.6 K hotter. The slope of this line is Rth.
Notes: Each point is one gate voltage of the V_D = 0.7 V Atlas sweep, plotted as temperature rise against dissipated power. At the on point R_th = 2.27 × 10⁶ K/W.

## Slide 94
Self-heating – Heat changes every metric
Turn the temperature knob and watch the switch get worse
300
325
350
375
400
50 %
60 %
70 %
80 %
90 %
100 %
channel temperature T (K)
mobility μ(T) / μ(300 K)
μ = 100 %
mobility μ (μ ∝ T⁻²)
100 %
Ion → slower circuit
base
SS limit (kT/q)·ln10
59.5
Ioff → more power
base
VT (≈ −1.6 mV/K)
0 mV
ageing (HCD, BTI)
base
KNOB: channel temperature T 300 K
300
325
350
375
400
At 300 K the device behaves as designed.
Notes: Mobility follows roughly T to the minus 2. This is why the project lowers ΔT: a cooler channel keeps I_on, SS and I_off healthy.

## Slide 95
Self-heating – Heat changes every metric
Turn the temperature knob and watch the switch get worse
300
325
350
375
400
50 %
60 %
70 %
80 %
90 %
100 %
channel temperature T (K)
mobility μ(T) / μ(300 K)
μ = 76 %
343.6 K = peak of our reproduced device
mobility μ (μ ∝ T⁻²)
76 % ▼
Ion → slower circuit
falls ▼
SS limit (kT/q)·ln10
68.2 ▲
Ioff → more power
rises ▲
VT (≈ −1.6 mV/K)
−70 mV ▼
ageing (HCD, BTI)
faster ▲
KNOB: channel temperature T 343.6 K
300
325
350
375
400
At our reproduced peak, 343.6 K, mobility is already 24 % lower.
Notes: Mobility follows roughly T to the minus 2. This is why the project lowers ΔT: a cooler channel keeps I_on, SS and I_off healthy.

## Slide 96
Self-heating – Heat changes every metric
Turn the temperature knob and watch the switch get worse
300
325
350
375
400
50 %
60 %
70 %
80 %
90 %
100 %
channel temperature T (K)
mobility μ(T) / μ(300 K)
μ = 56 %
mobility μ (μ ∝ T⁻²)
56 % ▼
Ion → slower circuit
falls ▼
SS limit (kT/q)·ln10
79.4 ▲
Ioff → more power
rises ▲
VT (≈ −1.6 mV/K)
−160 mV ▼
ageing (HCD, BTI)
faster ▲
KNOB: channel temperature T 400 K
300
325
350
375
400
At 400 K the switch is slower, leakier and ages faster.
Notes: Mobility follows roughly T to the minus 2. This is why the project lowers ΔT: a cooler channel keeps I_on, SS and I_off healthy.

## Slide 97
Self-heating – What heat does to the current
Heat helps a little below 0.57 V and hurts above it [4]
0.3
0.4
0.5
0.6
0.7
0 µA
10 µA
20 µA
30 µA
gate voltage VGS (V)
ID (schematic)
cross at 0.57 V
without self-heating
with self-heating
VGS < 0.57 V: ID slightly up
Heat creates extra electron–hole pairs (SRH generation), adding a little current.
VGS > 0.57 V: Ion down
Hot lattice → more phonon scattering → mobility μ falls, worst at the source end → less Ion.
Schematic of the trend reported by Kang et al. [4] (exaggerated for clarity).
In the on-state heat lowers mobility and Ion: that is the loss our project fights.
Notes: Below about 0.57 V heat adds a little generation current; above it, mobility loss dominates and on-current drops.

## Slide 98
Self-heating – Thermal crosstalk
A hot transistor heats its neighbour through the shared gate metal and substrate
shared gate metal and substrate
NMOS on
ΔTSH = 64.8 K
PMOS off
ΔTcross = 22.4 K
heat
Crosstalk coefficient
α = ΔTcross / ΔTSH
= 22.4 / 64.8 = 34.6 %
base paper [1]
About a third of the hot device's rise reaches the device next to it. Lowering self-heating at the source lowers crosstalk with it.
Self-heating first, then crosstalk: our project builds on the first.
Notes: Transistors in a cell share the gate metal and the substrate. Heat from the active NMOS spreads into the PMOS next to it, even though the PMOS is off.

## Slide 99
Contents
01
The MOSFET switch
Build it · turn the gate · turn the drain · VT and SS in depth
02
Shrinking the gate
Shorter Lg · DIBL and leakage · the scale length λ
03
FinFET → GAAFET
More gate sides · fin width · wire, sheet, stack · our GAA in numbers
04
The new problem: heat
Oxide traps heat · ΔT = Rth · P · what heat does to every metric
05
Literature and method
Five papers · base paper Chen et al. 2025 · Silvaco Atlas flow
06
Three stages in TCAD
Standard GAAFET · reproduce the paper · optimal design D
07
Conclusion
Gains and limits · the whole story · next steps
Chapter 05
Literature and method
Five papers
base paper Chen et al. 2025
Silvaco Atlas flow
Notes: Chapter 5: what others found, and how we simulate.

## Slide 100
Literature review – Five papers
Where the heat goes in GAA devices, and how to lower it
# | Paper | Method | Key finding
[1] | Chen et al., IEEE EDTM 2025 | Thermal TCAD, 3-nm GAA cells | NMOS self-heats 64.8 K at 30 µW; crosstalk 34.6 %
[2] | Rathore et al., IEEE TED 2023 | Calibrated TCAD, nanosheet FET | DLC buried oxide: peak 626 K → 442 K
[3] | Cai et al., VLSI-TSA 2018 | 3D simulation, stacked nanosheets | Up to 128 K rise; ~40 % of heat leaves via the substrate
[4] | Kang et al., IEEE TED 2022 | 3D TCAD, 3 stacked GAA nanowires | Wrap-around W contact: Rth 5.27 → 4.83 K/µW, Ion 1.74×
[5] | Belkhiria et al., SSD 2021 | Heat model, linear doping | Work function and doping set the temperature
Lever 1 – a better heat path: [2], [3], [4]: put a high-κ material next to the hot spot.
Lever 2 – less power: [5]: a small work-function shift lowers P.
Two levers keep appearing: a better heat path, or less power.
Notes: Chen is the base paper. Rathore and Cai show the substrate heat path, Kang shows that a metal contact around the source and drain lowers the thermal resistance, and Belkhiria shows that the work function sets the temperature.

## Slide 101
Literature review – Choosing the base paper
One paper to reproduce: it must match our project and give a clear target
Question | [1] Chen | [2] Rathore | [3] Cai | [4] Kang | [5] Belkhiria
Published by IEEE | ✓ | ✓ | ✓ | ✓ | ✓
About thermal crosstalk (our title) | ✓ | – | – | – | –
One clear number to match | ✓ | ✓ | ✓ | ✓ | –
All sizes and κ values given | ✓ | ✓ | – | ✓ | –
Single GAA device we can simulate | ✓ | – | – | – | ✓
Score | 5/5 | 3/5 | 2/5 | 3/5 | 2/5
Why Chen? It is the only paper that scores 5/5: it studies thermal crosstalk, our title, gives one clear number to match, and has a single GAA device we can simulate.
Base paper: Chen et al., IEEE EDTM 2025. The other four support it.
Notes: We compared the papers on five questions. Chen et al. is the only one about thermal crosstalk in GAA, our project title, with one clear number and every dimension and conductivity in its Table I.

## Slide 102
Literature review – Base paper [1]
Chen et al.: in an inverter the active NMOS heats the PMOS next to it
VDD
PMOS
off
NMOS
on · 30 µW
VSS
in = 1
out = 0
heat
64.8 K
NMOS self-heating at 30 µW
22.4 K
PMOS rise from crosstalk
34.6 %
crosstalk coefficient α (31.7 % the other way)
A single GAAFET with the same substrate runs about 6 K hotter than the NMOS inside the inverter, because the PMOS helps carry its heat away.
One number to reproduce: 64.8 K at 30 µW.
Notes: In a 6-track inverter with input 1, the NMOS is on and dissipates 30 microwatts. It heats itself by 64.8 K. The PMOS is off, but heat through the shared gate raises it by 22.4 K.

## Slide 103
Literature review – Base paper [1]
More active neighbours, more crosstalk heating
Chart: Temperature rise of the target device above 300 K (%)
| Inverter (2 devices) | 3 active devices | 4 active devices
rise | 7.5 | 11.8 | 14.9
322.4 K
inverter PMOS (+7.5 %)
335.3 K
three active devices (+11.8 %)
344.6 K
four active devices (+14.9 %)
Crosstalk grows with device density: a reason to cut self-heating at the source.
Notes: With two, three and four active devices the target heats by 7.5, 11.8 and 14.9 percent above ambient.

## Slide 104
Literature review – Table I of the base paper
The geometry and materials we copy into our deck
Dimension | Value (nm)
Channel length Lg | 14
Nanosheet width | 20
Nanosheet thickness | 5
Gate oxide thickness | 1.1
Sub-fin thickness | 40
Metal-2 pitch (inverter) | 21
Material | κ (W/m·K)
N-channel Si | [22, 22, 6]
P-channel SiGe | [18, 18, 4]
Gate HfO2 | 2.3
Interface oxide | 1.4
Copper | 385
Si substrate | 148
20 × 5 nm nanosheet (to scale)
Same Lg, oxide and κ values as the paper; only the channel shape differs.
Notes: Geometry and thermal conductivity values from Table I of the base paper. We use the same gate length, oxide thickness and conductivities.

## Slide 105
Literature review – A better heat exit [2], [3]
Giving the heat a better way out lowers the peak temperature
Rathore et al. [2]: DLC as buried oxide
Chart: Peak lattice temperature (K)
| SiO₂ BOX | DLC BOX
T | 626 | 442
Cai et al. [3]: stacked nanosheets
128 K
self-heating rise at VG = VD = 0.7 V
~40 %
of the heat leaves through the substrate
−40 K
with higher-κ substrate or interconnect materials
Lever 1: replace a low-κ layer next to the heat with a high-κ one.
Notes: Rathore replaced the SiO2 buried oxide with diamond-like carbon and the peak lattice temperature fell from about 626 K to 442 K. Cai found that about 40 percent of the heat leaves through the substrate.

## Slide 106
Literature review – The contact as a heat path [4]
Kang et al., TED 2022: 3 stacked GAA nanowires, top contact vs wrap-around contact
ILD (SiO₂, 1.4 W/m·K)
S
D
gate (TiN)
ground plane
W metal (grey) on top only
5.27
Rth (K/µW)
1
Ion (× TC)
112
contact area (nm²)
TC
WAC
Rth = (Tmax − Tmin) / total heat: the same slope method as our ΔT–P line
Top contact: heat and current must travel up the source and drain to a small metal pad.
Notes: Kang et al. compare a top contact with a wrap-around contact in a three-wire GAA stack. Metal around the source and drain lowers the thermal resistance by about ten percent.

## Slide 107
Literature review – The contact as a heat path [4]
Kang et al., TED 2022: 3 stacked GAA nanowires, top contact vs wrap-around contact
ILD (SiO₂, 1.4 W/m·K)
S
D
gate (TiN)
ground plane
W metal (grey) wraps S and D
5.27
4.83
Rth (K/µW)
1
1.74
Ion (× TC)
112
1579
contact area (nm²)
TC
WAC
Rth = (Tmax − Tmin) / total heat: the same slope method as our ΔT–P line
Wrap-around contact: tungsten (174 W/m·K) touches the hot drain directly: Rth −9.7 %, Ion 1.74×.
Notes: Kang et al. compare a top contact with a wrap-around contact in a three-wire GAA stack. Metal around the source and drain lowers the thermal resistance by about ten percent.

## Slide 108
Literature review – Our plan
Three stages on one Atlas deck, each building on the last
1
Standard GAAFET
r = 4 nm wire, α = 5000
Check that the deck runs and the electrostatics are sound.
→
2
Reproduce base paper
r = 5.64 nm, α = 59 000
Match the paper's Rth: 64.8 K at 30 µW.
→
3
Optimal GAAFET
spacer κ 60, WF 4.53 eV
Lower ΔT with Ion within 10 % and Ioff no worse.
Standard → reproduced → optimal, all on one Atlas deck.
Notes: Stage 1 builds a standard device to check the deck. Stage 2 changes it until it heats like the base paper. Stage 3 uses the two levers from the literature to make it cooler.

## Slide 109
Methodology – TCAD flow
Every result comes from the same five steps in Silvaco Atlas
01
Mesh
cylindrical 3D grid in r, angle, z
→
02
Regions
Si, SiO2, HfO2, W, Si3N4, contacts
→
03
Doping
n+ S/D 10²⁰, ext 10¹⁹, channel p 10¹⁶
→
04
Models + solve
drift-diffusion + heat, VG sweep
→
05
Extract
VT, SS, DIBL, Ion, Ioff, Tmax
Tools: Atlas 5.28.1.R (device + lattice heat) · DeckBuild (deck + extract) · TonyPlot (plots)
One deck, five steps; only a few lines change between stages.
Notes: We write one Atlas input deck. It defines the mesh and regions, sets doping, chooses physical models, solves for voltage sweeps, and extracts the numbers in DeckBuild.

## Slide 110
Methodology – What Atlas solves
Electricity and heat are solved together, because each changes the other
Poisson
potential ψ
Electron continuity
current Jn
Joule heat
H = J · E
Heat equation
lattice temp. TL
Mobility μ(T)
fldmob, cvt
1
Poisson: the gate sets the potential
Solves for ψ everywhere: the energy hill under the gate.
Atlas first finds the potential.
Notes: Solves for ψ everywhere: the energy hill under the gate.

## Slide 111
Methodology – What Atlas solves
Electricity and heat are solved together, because each changes the other
Poisson
potential ψ
Electron continuity
current Jn
Joule heat
H = J · E
Heat equation
lattice temp. TL
Mobility μ(T)
fldmob, cvt
2
Current from the potential
Electrons drift and diffuse: current Jn. Same physics as the ID–VG curves.
The potential drives the current.
Notes: Electrons drift and diffuse: current J_n. Same physics as the I_D–V_G curves.

## Slide 112
Methodology – What Atlas solves
Electricity and heat are solved together, because each changes the other
Poisson
potential ψ
Electron continuity
current Jn
Joule heat
H = J · E
Heat equation
lattice temp. TL
Mobility μ(T)
fldmob, cvt
3
Current makes heat
Every bit of current loses energy, H = J · E, most of it near the drain.
Current turns into heat.
Notes: Every bit of current loses energy, H = J · E, most of it near the drain.

## Slide 113
Methodology – What Atlas solves
Electricity and heat are solved together, because each changes the other
Poisson
potential ψ
Electron continuity
current Jn
Joule heat
H = J · E
Heat equation
lattice temp. TL
Mobility μ(T)
fldmob, cvt
4
Heat raises the temperature
The heat equation spreads H through all regions; each material has its own κ.
Heat raises the lattice temperature.
Notes: The heat equation spreads H through all regions; each material has its own κ.

## Slide 114
Methodology – What Atlas solves
Electricity and heat are solved together, because each changes the other
Poisson
potential ψ
Electron continuity
current Jn
Joule heat
H = J · E
Heat equation
lattice temp. TL
Mobility μ(T)
fldmob, cvt
5
Hot lattice slows electrons
Mobility falls as T rises → less current. The loop closes: Atlas repeats until it settles.
Temperature changes the current again: a loop.
Notes: Mobility falls as T rises → less current. The loop closes: Atlas repeats until it settles.

## Slide 115
Methodology – What Atlas solves
Electricity and heat are solved together, because each changes the other
Poisson
potential ψ
Electron continuity
current Jn
Joule heat
H = J · E
Heat equation
lattice temp. TL
Mobility μ(T)
fldmob, cvt
heat exit α → 300 K
6
Heat must leave somewhere
thermcontact on S, D, G at 300 K. α (W/cm²·K): larger α = easier exit = cooler.
Heat leaves through the contacts: the heat-exit α we calibrate.
Notes: thermcontact on S, D, G at 300 K. α (W/cm²·K): larger α = easier exit = cooler.

## Slide 116
Methodology – Choosing the solver
How we made a 3D electro-thermal run fit on a laptop
✗
Gummel
heat residual stuck at 10¹⁹: no I–V data
✗
Full Newton
4 coupled equations, 174k nodes: memory allocation failure
✓
Block Newton, 1 carrier
heat solved in its own block, 24k nodes: 15–35 min per run
models cvt srh auger bgn fldmob lat.temp
thermcontact num=1 elec.num=1 \
ext.temp=300 alpha=5000
method block newton carriers=1 electrons
probe name=Tmax lat.temp max
Block Newton with one carrier makes 3D self-heating practical.
Notes: Gummel could not converge the heat equation, and the fully coupled Newton ran out of memory. Block Newton with electrons only solves the heat equation separately and needs far less memory.

## Slide 117
Methodology – Every number from two curves
The transfer curve gives the electrical metrics; the heat curve gives Rth
0
0.2
0.4
0.6
100 pA
10 nA
1 µA
100 µA
VG (V)
ID (log)
Ioff: VG = 0
VT: max-gm extrapolation
SS: mV per ×10
DIBL: shift ÷ 0.65 V
Ion: VG = VD = 0.7 V
Two transfer curves
VD = 0.05 V (teal) and 0.7 V (blue), VG swept 0 → 0.7 V.
From them: VT, SS, DIBL, Ion and Ioff.
Transfer curves: VT, SS, DIBL, Ion and Ioff.
Notes: Every number we report is read from these two kinds of curve.

## Slide 118
Methodology – Every number from two curves
The transfer curve gives the electrical metrics; the heat curve gives Rth
0
0.2
0.4
0.6
100 pA
10 nA
1 µA
100 µA
VG (V)
ID (log)
Ioff: VG = 0
VT: max-gm extrapolation
SS: mV per ×10
DIBL: shift ÷ 0.65 V
Ion: VG = VD = 0.7 V
0
5
10
15
20
0
25
50
P = ID · VD (µW)
ΔT (K)
Rth = ΔT / P = slope
= 2.27 × 10⁶ K/W
Tmax: probe lat.temp max; ΔT = Tmax − 300 K
Heat curve: Rth is the slope of ΔT against power.
Notes: Every number we report is read from these two kinds of curve.

## Slide 119
Contents
01
The MOSFET switch
Build it · turn the gate · turn the drain · VT and SS in depth
02
Shrinking the gate
Shorter Lg · DIBL and leakage · the scale length λ
03
FinFET → GAAFET
More gate sides · fin width · wire, sheet, stack · our GAA in numbers
04
The new problem: heat
Oxide traps heat · ΔT = Rth · P · what heat does to every metric
05
Literature and method
Five papers · base paper Chen et al. 2025 · Silvaco Atlas flow
06
Three stages in TCAD
Standard GAAFET · reproduce the paper · optimal design D
07
Conclusion
Gains and limits · the whole story · next steps
Chapter 06
Three stages in TCAD
Standard GAAFET
reproduce the paper
optimal design D
Notes: Chapter 6: build, reproduce, optimise.

## Slide 120
Stage 1 – Standard GAAFET, layer by layer
Step 1: the silicon wire · A silicon cylinder, radius 4 nm, 58 nm long
cross-section at the gate
r = 4 nm
side view along the current (z)
17 nm
5 nm
14 nm
5 nm
17 nm
Si channel
SiO2
HfO2
W gate
Si3N4
n+ Si
REGION NUM=1 MATERIAL=silicon R.MAX=0.004 Z.MIN=-0.029 Z.MAX=0.029
Everything starts from one silicon wire.
Notes: Start with a 4 nm radius silicon wire along z. Source, extensions, channel and drain are all part of it.

## Slide 121
Stage 1 – Standard GAAFET, layer by layer
Step 2: interfacial oxide · A 0.6 nm SiO2 shell around the channel only
cross-section at the gate
r = 4 nm
side view along the current (z)
17 nm
5 nm
14 nm
5 nm
17 nm
Si channel
SiO2
HfO2
W gate
Si3N4
n+ Si
REGION NUM=2 MATERIAL=oxide R.MIN=0.004 R.MAX=0.0046 Z.MIN=-0.007 Z.MAX=0.007
The oxide sits only under the gate.
Notes: A thin SiO2 layer sits on the silicon under the gate. It gives a clean interface but conducts heat poorly: 1.4 W/m K.

## Slide 122
Stage 1 – Standard GAAFET, layer by layer
Step 3: high-κ dielectric · A 1.1 nm HfO2 shell, as in Table I
cross-section at the gate
r = 4 nm
side view along the current (z)
17 nm
5 nm
14 nm
5 nm
17 nm
Si channel
SiO2
HfO2
W gate
Si3N4
n+ Si
REGION NUM=3 MATERIAL=HfO2 R.MIN=0.0046 R.MAX=0.0057 Z.MIN=-0.007 Z.MAX=0.007
High-κ for gate control; low κ for heat.
Notes: HfO2 has a high dielectric constant (22), so the gate couples strongly to the channel. Its thermal conductivity is only 2.3 W/m K.

## Slide 123
Stage 1 – Standard GAAFET, layer by layer
Step 4: gate and spacers · A 3 nm tungsten gate, Si3N4 spacers, oxide over S/D
cross-section at the gate
r = 4 nm
side view along the current (z)
17 nm
5 nm
14 nm
5 nm
17 nm
Si channel
SiO2
HfO2
W gate
Si3N4
n+ Si
REGION NUM=8 MATERIAL=tungsten R.MIN=0.0057 R.MAX=0.0087 · REGION NUM=4/5 MATERIAL=nitride Z=±(0.007–0.012)
The gate now wraps the channel on all sides.
Notes: The gate metal wraps the stack over the 14 nm gate. Silicon nitride spacers separate the gate from the source and drain extensions.

## Slide 124
Stage 1 – Standard GAAFET, layer by layer
Step 5: doping, contacts, heat exits · n+ source/drain, p channel; three electrodes at 300 K
cross-section at the gate
r = 4 nm
side view along the current (z)
source · 300 K
gate · 300 K
drain · 300 K
17 nm
5 nm
14 nm
5 nm
17 nm
Si channel
SiO2
HfO2
W gate
Si3N4
n+ Si
doping n.type 1e20 (S/D), 1e19 (ext), p.type 1e16 · thermcontact elec.num=1..3 ext.temp=300 alpha=5000
The standard device is complete.
Notes: Source and drain are doped n plus, the extensions slightly less, the channel lightly p type. Source, drain and gate are heat contacts at 300 K with alpha 5000.

## Slide 125
Stage 1 – Electrical result
Standard GAAFET: a near-ideal switch
0.209 V
VT (linear)
61.3 mV/dec
subthreshold swing
17.3 mV/V
DIBL
17.9 µA
Ion at VG = VD = 0.7 V
99 pA
Ioff
12.5 µW
Pon = Ion × 0.7 V
Electrically, the standard device is sound.
Notes: The standard device switches with a subthreshold swing of 61.3 mV per decade, close to the 60 mV limit, and DIBL of 17.3 mV per volt.

## Slide 126
Stage 1 – Thermal result
Far too hot compared with the paper
Chart: Temperature rise at 30 µW (K)
| Base paper | Our standard device
ΔT | 64.8 | 727
603 K
peak lattice temperature at the on point
2.42 × 10⁷
Rth in K/W (paper: 2.16 × 10⁶)
11×
too hot compared with the base paper
Thermally wrong: the template heat exits let almost no heat out.
Notes: The peak lattice temperature is 603 K at 12.5 microwatts. Scaled to 30 microwatts this is a 727 K rise, eleven times the paper.

## Slide 127
Stage 2 – What is different from the paper?
Line-by-line comparison of our standard device with the base paper
Item | Base paper | Our standard device | Same?
Gate length | 14 nm | 14 nm | ✓
Gate oxide | 1.1 nm HfO2 | 1.1 nm HfO2 + 0.6 nm SiO2 | ✓
κ values | Table I | Table I | ✓
Channel | 20 × 5 nm sheet = 100 nm² | wire r = 4 nm = 50 nm² | ✗ change 1
Heat exit | Si substrate, copper wiring | contacts with α = 5000 | ✗ change 2
Two changes: the channel area and the heat exit.
Notes: Gate length, oxide thickness and conductivities already match. Two things do not: the channel shape and how easily heat leaves the device.

## Slide 128
Stage 2 – Change 1: the channel area
Keep Atlas cylindrical, but give the wire the same silicon area as the paper's sheet
grey outline: old wire r = 4 nm
Paper: 20 × 5 nm nanosheet = 100 nm²
silicon area
100 nm²
radius r
–
Weff (perimeter)
50 nm
Why area matters
The same current in less silicon gives more heat per volume. So we match the area first, then the heat exit.
The paper's channel holds 100 nm² of silicon; our 4 nm wire only 50 nm².
Notes: Pi r squared equals 100 square nanometres, so r is 5.64 nm. All oxide and gate shells move out by the same amount.

## Slide 129
Stage 2 – Change 1: the channel area
Keep Atlas cylindrical, but give the wire the same silicon area as the paper's sheet
grey outline: old wire r = 4 nm
π r² = 100 nm² → r = 5.64 nm
silicon area
100 nm²
radius r
5.64 nm ▲
Weff (perimeter)
35.4 nm ▼
Shells moved out
SiO2 5.64–6.24 nm
HfO2 6.24–7.34 nm
W gate 7.34–10.34 nm
Same silicon area, so the same heat per volume.
Notes: Pi r squared equals 100 square nanometres, so r is 5.64 nm. All oxide and gate shells move out by the same amount.

## Slide 130
Stage 2 – Change 2: the heat exit α
Fit from our α sweep: Rth = 0.714 × 10⁶ + 9.18 × 10¹⁰ / α (K/W, α in W/cm²·K)
Rexit = 18.36 × 10⁶
Rinside = 0.71 × 10⁶ (oxides, gate, silicon: fixed)
share of the exit: 96 %
0k
20k
40k
60k
80k
0
50
100
150
200
heat exit α (W/cm²·K)
ΔT at 30 µW (K)
base paper 64.8 K
572 K ↑ off scale
Rth (K/W)
19.07 × 10⁶
ΔT at 30 µW
572.2 K
vs paper
+783 %
KNOB: heat exit α 5k
5k
30k
59k
80k
With the template α = 5000 the contact exit is 96 % of Rth: the heat can barely leave.
Notes: Solving for the paper's R_th exactly gives α ≈ 63 500. We had already run 59 000, which is within 5 %, and kept it so all later designs compare on the same heat exit. The α = 5000 point here is for the r = 5.64 nm wire; the r = 4 nm template device gave 727 K.

## Slide 131
Stage 2 – Change 2: the heat exit α
Fit from our α sweep: Rth = 0.714 × 10⁶ + 9.18 × 10¹⁰ / α (K/W, α in W/cm²·K)
Rexit = 1.84 × 10⁶
Rinside = 0.71 × 10⁶ (oxides, gate, silicon: fixed)
share of the exit: 72 %
0k
20k
40k
60k
80k
0
50
100
150
200
heat exit α (W/cm²·K)
ΔT at 30 µW (K)
base paper 64.8 K
76.5 K
Rth (K/W)
2.55 × 10⁶ ▼
ΔT at 30 µW
76.5 K ▼
vs paper
+18 % ▼
KNOB: heat exit α 50k
5k
30k
59k
80k
First guess α = 50 000: ΔT = 76.4 K, still 18 % above the paper.
Notes: Solving for the paper's R_th exactly gives α ≈ 63 500. We had already run 59 000, which is within 5 %, and kept it so all later designs compare on the same heat exit. The α = 5000 point here is for the r = 5.64 nm wire; the r = 4 nm template device gave 727 K.

## Slide 132
Stage 2 – Change 2: the heat exit α
Fit from our α sweep: Rth = 0.714 × 10⁶ + 9.18 × 10¹⁰ / α (K/W, α in W/cm²·K)
Rexit = 1.56 × 10⁶
Rinside = 0.71 × 10⁶ (oxides, gate, silicon: fixed)
share of the exit: 69 %
0k
20k
40k
60k
80k
0
50
100
150
200
heat exit α (W/cm²·K)
ΔT at 30 µW (K)
base paper 64.8 K
68.1 K
Rth (K/W)
2.27 × 10⁶ ▼
ΔT at 30 µW
68.1 K ▼
vs paper
+5 % ▼
KNOB: heat exit α 59k
5k
30k
59k
80k
α = 59 000: Rth = 2.27 × 10⁶ K/W, within 5 % of the paper; kept for every later design.
Notes: Solving for the paper's R_th exactly gives α ≈ 63 500. We had already run 59 000, which is within 5 %, and kept it so all later designs compare on the same heat exit. The α = 5000 point here is for the r = 5.64 nm wire; the r = 4 nm template device gave 727 K.

## Slide 133
Stage 2 – Reproduced device: transfer curves
Silvaco Atlas, r = 5.64 nm, α = 59 000, VD = 0.05 V and 0.7 V
0
0.1
0.2
0.3
0.4
0.5
0.6
0.7
100 pA
10 nA
1 µA
100 µA
gate voltage VG (V)
ID (log)
VD = 0.7 V
VD = 0.05 V
VT (linear)
0.204 V
subthreshold swing
65.4 mV/dec
Ion
27.5 µA
Ioff
624 pA
Pon = 27.5 µA × 0.7 V = 19.2 µW
Still a clean switch after the changes; the larger wire carries more current.
Notes: These are the Atlas I-V curves of the reproduced device. The larger wire carries more current than the standard one and swings at 65.4 mV per decade.

## Slide 134
Stage 2 – Reproduced: it heats like the paper
Temperature rise scaled to the paper's 30 µW (log scale)
Chart: 
| Base paper | Standard | Reproduced
ΔT | 64.8 | 727 | 68
343.6 K
peak at 19.2 µW
68.0 K
ΔT scaled to 30 µW (paper 64.8 K)
+5.0 %
error vs the base paper
Reproduced within 5 %, down from 11× too hot.
Notes: At its own on point the reproduced device reaches 343.6 K with 19.2 microwatts. Scaled to 30 microwatts that is 68.0 K, five percent above the paper.

## Slide 135
Stage 3 – Which knobs lower ΔT = Rth · P?
Two ways to cool: a better heat path (Rth) or less power (P)
ΔT = Rth × P
lower Rth: a better heat path
lower P: less power
Two ways to cool: lower Rth or lower P.
Notes: We looked for knobs that lower either factor without changing the device too much.

## Slide 136
Stage 3 – Which knobs lower ΔT = Rth · P?
Two ways to cool: a better heat path (Rth) or less power (P)
ΔT = Rth × P
lower Rth: a better heat path
Spacer κ ↑
Si₃N₄ → high-κ (thermal): heat leaves sideways into the gate
✓ lever 1
Buried oxide → DLC [2]
needs a substrate, not in our single wire
future
lower P: less power
Rth knob: a better heat path, the spacer.
Notes: We looked for knobs that lower either factor without changing the device too much.

## Slide 137
Stage 3 – Which knobs lower ΔT = Rth · P?
Two ways to cool: a better heat path (Rth) or less power (P)
ΔT = Rth × P
lower Rth: a better heat path
Spacer κ ↑
Si₃N₄ → high-κ (thermal): heat leaves sideways into the gate
✓ lever 1
Buried oxide → DLC [2]
needs a substrate, not in our single wire
future
lower P: less power
Gate work function ↑
4.50 → 4.53 eV: VT up → less current, less leakage
✓ lever 2
Supply VDD ↓
slower circuit, changes the operating point
✗
Rejected: a thinner or shorter channel (more heat per volume, changes the electrostatics).
Two clean knobs: spacer κ for Rth, work function for P.
Notes: We looked for knobs that lower either factor without changing the device too much.

## Slide 138
Stage 3 – Lever 1: a high-κ spacer
The spacer touches the gate metal, a heat contact at 300 K, only 5 nm from the channel
source · 300 K
gate · 300 K
drain · 300 K
17 nm
5 nm
14 nm
5 nm
17 nm
Si₃N₄ spacer (18 W/m·K)
1
Old path
Along the wire to the drain contact, 17 nm of silicon away. The nitride spacer (18 W/m·K) blocks the short way up.
spacer κ
18 W/m·K
ΔT change
0
Ion change
0
KNOB: spacer thermal conductivity 18 W/m·K
18
40
60
material nitride tc.const = 0.18 → 0.6 W/cm·K
The hot spot is at the drain end; its heat has a long way out.
Notes: With nitride spacers at 18 W/m K the heat must travel along the wire to the drain contact. A 60 W/m K spacer lets it move sideways into the gate metal, which is a heat contact.

## Slide 139
Stage 3 – Lever 1: a high-κ spacer
The spacer touches the gate metal, a heat contact at 300 K, only 5 nm from the channel
source · 300 K
gate · 300 K
drain · 300 K
17 nm
5 nm
14 nm
5 nm
17 nm
high-κ spacer (60 W/m·K)
2
New path
Up through the 5 nm spacer into the gate metal, a heat contact at 300 K. The current does not change: the spacer is outside the channel.
spacer κ
60 W/m·K ▲
ΔT change
−10.6 % ▼
Ion change
−0.1 %
KNOB: spacer thermal conductivity 60 W/m·K
18
40
60
material nitride tc.const = 0.18 → 0.6 W/cm·K
Spacer κ 18 → 60 W/m·K: Rth falls, current unchanged.
Notes: With nitride spacers at 18 W/m K the heat must travel along the wire to the drain contact. A 60 W/m K spacer lets it move sideways into the gate metal, which is a heat contact.

## Slide 140
Stage 3 – Lever 2: a slightly higher work function
Raise φm by 0.03 eV: VT goes up, so the same bias draws less power
0
0.1
0.2
0.3
0.4
0.5
0.6
0.7
100 pA
10 nA
1 µA
100 µA
gate voltage VG (V)
ID at VD = 0.7 V (log)
reproduced, WF 4.50 eV
VT
0.204 V
Ioff
624 pA
Ion
27.5 µA
Pon
19.2 µW
Reproduced device, before the shift.
KNOB: gate work function φm 4.50 eV
4.50
4.53
4.55
The work function sets VT one-to-one: our power knob.
Notes: Raising the gate work function from 4.50 to 4.53 eV raises the threshold by about 30 mV. At the same gate voltage the device carries less current, so P falls, and so does the temperature.

## Slide 141
Stage 3 – Lever 2: a slightly higher work function
Raise φm by 0.03 eV: VT goes up, so the same bias draws less power
0
0.1
0.2
0.3
0.4
0.5
0.6
0.7
100 pA
10 nA
1 µA
100 µA
gate voltage VG (V)
ID at VD = 0.7 V (log)
reproduced, WF 4.50 eV
design D, WF 4.53 eV
VT
0.233 V ▲
Ioff
246 pA ▼
Ion
25.3 µA ▼
Pon
17.7 µW ▼
+29 mV VT · 2.5× less leakage · −7.8 % Ion
KNOB: gate work function φm 4.53 eV
4.50
4.53
4.55
Less power P gives a lower ΔT = Rth · P, and leakage falls too.
Notes: Raising the gate work function from 4.50 to 4.53 eV raises the threshold by about 30 mV. At the same gate voltage the device carries less current, so P falls, and so does the temperature.

## Slide 142
Stage 3 – Four designs on the calibrated deck
Rule: lowest ΔT with Ion within 10 % of the reproduced device and Ioff no worse
Chart: Change vs the reproduced device (%)
| A spacer | B WF 4.55 | C A+B | D spacer+4.53
ΔT change (%) | -10.6 | -10.6 | -20.3 | -16.4
I_on change (%) | -0.1 | -12.9 | -13 | -7.8
Design | ΔT (K) | Ioff (pA) | Rule
Reproduced | 43.6 | 624 | –
A | 39.0 | 624 | Ioff same
B | 39.0 | 141 | Ion −12.9 %
C | 34.8 | 141 | Ion −13 %
D | 36.4 | 246 | all met
Why D? B and C lose more than 10 % Ion; A passes the rule but runs 2.6 K hotter.
D: 16.4 % cooler with Ion −7.8 %: the best trade-off.
Notes: A uses only the spacer, B only a larger work-function step of 4.55 eV, C both, and D the spacer with a smaller step of 4.53 eV.

## Slide 143
Stage 3 – Design D runs cooler at every bias
Peak lattice temperature against VG at VD = 0.7 V (Silvaco Atlas)
0
0.1
0.2
0.3
0.4
0.5
0.6
0.7
300
310
320
330
340
350
gate voltage VG (V)
Tmax (K)
reproduced 343.6 K
design D 336.4 K
336.4 K
peak (reproduced: 343.6 K)
−7.2 K
ΔT 43.6 → 36.4 K (−16.4 %)
2.06 × 10⁶
Rth in K/W (reproduced 2.27 × 10⁶)
D runs 7.2 K cooler at the same bias.
Notes: Design D stays below the reproduced device at every point and ends 7.2 K cooler, at 336.4 K.

## Slide 144
All three stages side by side
VDD = 0.7 V, Silvaco Atlas; base paper for reference
Metric | Standard | Reproduced | Optimal D | Base paper
Channel | wire r = 4 nm | wire r = 5.64 nm | wire r = 5.64 nm | sheet 20 × 5 nm
VT,lin (V) | 0.209 | 0.204 | 0.233 | –
SS (mV/dec) | 61.3 | 65.4 | 65.1 | –
Ion (µA) | 17.9 | 27.5 | 25.3 | –
Ioff (pA) | 99 | 624 | 246 | –
Pon (µW) | 12.5 | 19.2 | 17.7 | 30
Tmax (K) | 603.0 | 343.6 | 336.4 | –
Rth (K/W) | 2.42 × 10⁷ | 2.27 × 10⁶ | 2.06 × 10⁶ | 2.16 × 10⁶
ΔT at 30 µW (K) | 727 | 68.0 | 61.8 | 64.8
Reproduced within 5 %; optimal design 16.4 % cooler.
Notes: This table collects every number. The reproduced column matches the paper within 5 percent. The optimal column is cooler and leaks less, at a cost of 7.8 percent on-current.

## Slide 145
How every parameter changed along the way
One row per metric, one column per step of the story
 | Planar | FinFET | GAA | Standard | Reproduced | Optimal D
 | λ model, 14 nm | λ model, 14 nm | λ model, 14 nm | Atlas, r = 4 nm | Atlas, r = 5.64 nm | Atlas, r = 5.64 nm
λ (nm) | 4.37 | 2.52 | 2.18 | 2.18 | 2.59 | 2.59
SS (mV/dec) | 100 | 68 | 65 | 61.3 | 65.4 | 65.1
DIBL (mV/V) | 201 | 62 | 41 | 17.3 | 38 | ≈ 38
VT (V) | 0.01 | 0.24 | 0.28 | 0.209 | 0.204 | 0.233
Ioff | 241 nA | 144 pA | 26 pA | 99 pA | 624 pA | 246 pA
Ion (µA) | – | – | – | 17.9 | 27.5 | 25.3
ΔT at 30 µW (K) | – | – | – | 727 | 68.0 | 61.8
Gate sides fixed the electrostatics (λ, SS, DIBL); the heat exit and two small knobs fixed the temperature.
Each step changed one thing, and the numbers moved the way the physics says.
Notes: The first three columns are the simple scale-length model at a 14 nm gate with the same 8 nm silicon. The last three are Atlas results for our devices.

## Slide 146
Contents
01
The MOSFET switch
Build it · turn the gate · turn the drain · VT and SS in depth
02
Shrinking the gate
Shorter Lg · DIBL and leakage · the scale length λ
03
FinFET → GAAFET
More gate sides · fin width · wire, sheet, stack · our GAA in numbers
04
The new problem: heat
Oxide traps heat · ΔT = Rth · P · what heat does to every metric
05
Literature and method
Five papers · base paper Chen et al. 2025 · Silvaco Atlas flow
06
Three stages in TCAD
Standard GAAFET · reproduce the paper · optimal design D
07
Conclusion
Gains and limits · the whole story · next steps
Chapter 07
Conclusion
Gains and limits
the whole story
next steps
Notes: Chapter 7: what we gained, and what comes next.

## Slide 147
Conclusion – What the work gives, and what it costs
Advantages on the left, limitations on the right
Advantages
✓
Matches the base paper
68.0 K vs 64.8 K at 30 µW (+5 %).
✓
Cooler optimal device
−16.4 % ΔT, 2.5× less leakage, Ion −7.8 %.
✓
Runs on a laptop
Block Newton, 24k nodes, 15–35 min per device.
Limitations
!
Wire, not sheet
Equal area, but rounder than the 20 × 5 nm sheet.
!
Lumped heat exit
Substrate and copper wiring folded into one fitted α.
!
One device only
Crosstalk needs a second device in the deck.
A calibrated single-device model, ready to extend to crosstalk.
Notes: Advantages: we match the base paper, we have a cooler device, and the method runs on a laptop. Limitations: our channel is a wire not a sheet, the substrate and wiring are lumped into one alpha, and we model one device only.

## Slide 148
Conclusion – The whole story
From a leaking MOSFET to a cooler GAAFET, in five steps
1
MOSFET
short Lg leaks
DIBL 202 mV/V
2
GAAFET
gate on all sides
DIBL 17 mV/V
3
Heat
oxide traps it
ΔT 64.8 K
4
Reproduce
68.0 vs 64.8 K
+5 %
5
Optimal
spacer + WF
16.4 % cooler
Short planar transistors let the drain take over the channel.
Control fixed by GAA; heat lowered by design.
Notes: A one-slide recap: short MOSFETs leak, GAA fixes that, GAA traps heat, we reproduced the heat of the base paper, and we lowered it with a better spacer and a small work-function shift.

## Slide 149
Conclusion – The whole story
From a leaking MOSFET to a cooler GAAFET, in five steps
1
MOSFET
short Lg leaks
DIBL 202 mV/V
2
GAAFET
gate on all sides
DIBL 17 mV/V
3
Heat
oxide traps it
ΔT 64.8 K
4
Reproduce
68.0 vs 64.8 K
+5 %
5
Optimal
spacer + WF
16.4 % cooler
Wrapping the gate all round restores control: λ 4.37 → 2.18 nm.
Control fixed by GAA; heat lowered by design.
Notes: A one-slide recap: short MOSFETs leak, GAA fixes that, GAA traps heat, we reproduced the heat of the base paper, and we lowered it with a better spacer and a small work-function shift.

## Slide 150
Conclusion – The whole story
From a leaking MOSFET to a cooler GAAFET, in five steps
1
MOSFET
short Lg leaks
DIBL 202 mV/V
2
GAAFET
gate on all sides
DIBL 17 mV/V
3
Heat
oxide traps it
ΔT 64.8 K
4
Reproduce
68.0 vs 64.8 K
+5 %
5
Optimal
spacer + WF
16.4 % cooler
But the oxide that wraps the channel also traps its heat.
Control fixed by GAA; heat lowered by design.
Notes: A one-slide recap: short MOSFETs leak, GAA fixes that, GAA traps heat, we reproduced the heat of the base paper, and we lowered it with a better spacer and a small work-function shift.

## Slide 151
Conclusion – The whole story
From a leaking MOSFET to a cooler GAAFET, in five steps
1
MOSFET
short Lg leaks
DIBL 202 mV/V
2
GAAFET
gate on all sides
DIBL 17 mV/V
3
Heat
oxide traps it
ΔT 64.8 K
4
Reproduce
68.0 vs 64.8 K
+5 %
5
Optimal
spacer + WF
16.4 % cooler
Our Atlas GAAFET heats like the base paper, within 5 %.
Control fixed by GAA; heat lowered by design.
Notes: A one-slide recap: short MOSFETs leak, GAA fixes that, GAA traps heat, we reproduced the heat of the base paper, and we lowered it with a better spacer and a small work-function shift.

## Slide 152
Conclusion – The whole story
From a leaking MOSFET to a cooler GAAFET, in five steps
1
MOSFET
short Lg leaks
DIBL 202 mV/V
2
GAAFET
gate on all sides
DIBL 17 mV/V
3
Heat
oxide traps it
ΔT 64.8 K
4
Reproduce
68.0 vs 64.8 K
+5 %
5
Optimal
spacer + WF
16.4 % cooler
A high-κ spacer and a 0.03 eV work-function step make it 16.4 % cooler.
Control fixed by GAA; heat lowered by design.
Notes: A one-slide recap: short MOSFETs leak, GAA fixes that, GAA traps heat, we reproduced the heat of the base paper, and we lowered it with a better spacer and a small work-function shift.

## Slide 153
Conclusion – Next steps
From one hot device to thermal crosstalk between devices
1
Two devices
Place the calibrated GAAFET next to a second one on a shared substrate.
2
Crosstalk α
Measure ΔTcross / ΔTSH and compare with 34.6 % in the paper.
3
Geometry sweep
Gate oxide, BOX thickness and channel length vs Reff = ΔT / P.
4
Mitigation
High-κ BOX (DLC-type) [2] and metal heat paths such as wrap-around contacts [4].
Next: two devices, a shared substrate, and the crosstalk coefficient.
Notes: Next we place a second device beside the calibrated one, measure the crosstalk coefficient and compare it with the paper's 34.6 percent, then sweep geometry and try a high-conductivity buried oxide.

## Slide 154
References
[1] S. Chen, H. Wu, R. Wang, R. Huang, and L. Zhang, "Thermal crosstalk analysis in advanced CMOS circuits: Insights from 3nm gate-all-around transistor technology," in Proc. IEEE EDTM, 2025, doi: 10.1109/EDTM61175.2025.11040984.
[2] S. Rathore, R. K. Jaisawal, P. N. Kondekar, and N. Bagga, "Demonstration of a nanosheet FET with high thermal conductivity material as buried oxide: Mitigation of self-heating effect," IEEE Trans. Electron Devices, vol. 70, no. 4, pp. 1970–1976, Apr. 2023.
[3] L. Cai, W. Chen, G. Du, X. Zhang, and X. Liu, "Investigation of self-heating effect on stacked nanosheet GAA transistors," in Proc. VLSI-TSA, 2018, doi: 10.1109/VLSI-TSA.2018.8403821.
[4] S. J. Kang, J. H. Kim, Y. S. Song, S. Go, and S. Kim, "Investigation of self-heating effects in vertically stacked GAA MOSFET with wrap-around contact," IEEE Trans. Electron Devices, vol. 69, no. 3, pp. 910–914, Mar. 2022, doi: 10.1109/TED.2022.3140283.
[5] M. Belkhiria and F. Echouchene, "Analysis of heat transfer in GAAFET transistor with linear doping based on single-phase lag model," in Proc. SSD, 2021, doi: 10.1109/SSD52085.2021.9429320.
[6] Silvaco Inc., Atlas User's Manual, version 5.28.1.R.
Notes: Full references for the five papers and the simulator.

## Slide 155
Thank you
Questions and discussion
Nithyanand B · Priyadharshini K · Sivaprakash R
M.Tech VLSI Design · Analog VLSI and Device Modelling Lab (25VL681)